Preliminary Project Determinations

IEBC Work Class, IBC Use/Occupancy Class, Risk Level, PC/RC/NDC, etc.

Proposed work (aka projects) must receive preliminary determination of the following from the Facility Design Authority Representative (FDAR):

- IBC/IEBC scope?  Whether proposed work is subject to LANL’s program within the rules and examples in Tables IBC-GEN-1 & 2.

      - If FDAR determines not in IBC Program, no documentation is required; project may exit this process/chapter

      - If the FDAR has any uncertainty regarding this decision, they must consult the Chapter 16 POC

- If in scope, work classification(s) based on this form’s definitions in its instructions.

      - E.g., Repair, Alteration Level 1, Alt Level 2, Alt Level 3, Use or Occupancy Change, Addition, Historic, Relocation, Demolition, and/or New Building

- Determination of the risk level (H, M, L) per IBC-GEN Figure 1, IBC Program Three-Tiered Approach Flowchart

Requestor Input to FDAR

| Project Name/Location: |
| --- |
| Hazardous materials in occupancy (if yes, describe existing inventory and effect of project, or refer to and attach Form 2, HazMat Determination/ Chemical Inventory) |
| Estimated cost of work: |
| Statement of Work and proposed IEBC Ch. 4 Work Classification(s) – by subtasks if differing: Describe the proposed work with sufficient detail to allow proper classification per the choices given below. Subtasks may have different classifications (e.g., may be altering one system as Level 1 and another as Level 2). For IEBC Alt Level 2 and 3 adding additional loads on seismic-force-resisting SSCs, include enough detail that a judgment can be made on need for a feasibility study, or arrange for study prior to submission of this form. |
| Proposed IBC Ch. 3 Use and Occupancy Class(es) with rationale (N/A unless potentially changing from design basis or current levels): |
| Does work involve any special inspection tasks such as: ❐N/A fire barrier penetrations?❐ structural anchorage, concrete, steel, or masonry?❐ reroofing?❐ EIFS (synthetic stucco)? ❐ fire coatings?❐ other IBC Ch. 17 task?❐ (results in Moderate Risk as a minimum) |
| Risk level per IBC-GEN Figure 1, IBC Program Three-Tiered Approach Flowchart: ❐Highest ❐Moderate ❐Lowest |
| If self-perform, submittal reduction eligibility potential per ESM Ch. 1 Section Z10 Att. F criteria? ❐Yes ❐No |
| Eligible for sketches only (vs. drawings) per CAD Manual? ❐Yes ❐No |
| Existing facility mods: Qualifies for code of record design per criteria in IBC-GEN Att. B, LANL Existing Building Code ❐Yes ❐No ❐N/A If yes, COR date: _______________ |
| For IEBC Alt Level 2 and 3 adding additional loads on seismic-force-resisting SSCs, must a feasibility study be performed? ❐Yes ❐No |
| NPH: PC, RC, or NDC/LS category (see instructions for guidance): |
| Statement of Special Inspections per IBC-IP required by IBC 1704.3? ❐Yes ❐No |
| Sustainable design review required to ensure meets ESM Ch. 14? ❐Yes ❐No |
| Commissioning required per ESM Ch. 15? ❐Yes ❐No |
| Existing nuclear facility “major modification” ❐Yes ❐No ❐N/A |
| Other information helpful to determinations to be made: |
| Requester | Z Number | Organization | Date |
| Email | Phone |  | Code of Record date or intended IBC/IEBC Edition |

FDAR Action

❐Accept ❐ Accept with Modification:

| Name | Z Number | Signature | Date |
| --- | --- | --- | --- |

When “Repair” only: Remainder of this form is unneeded and need not be printed/retained as a record; also, other formal FDAR processes for determining IBC or not, being a repair, and repair risk level determinations equivalent to this form are acceptable.  If the FDAR has any uncertainty regarding being a “Repair”, form must proceed to C/S/A Team as described below.

When more than “Repair,” ES-EPD core team concurrence is required.

When work type is more than “Repair” per this form’s definition, the project shall gain concurrence from the LANL Building Official (LBO) Civil/Structural/Architectural Team Leader (ES-EPD).  Either the FDAR or Project transmits to ES EPD CSA Team (ESR preferred method).

Once issued, these determinations must then be included as preliminary design inputs somewhere in the statement of work for the design, noting that the designer retains responsibility for proposing more appropriate classifications as soon as they become evident.

Change Control: In addition to designer proposals noted above, Requester must submit a revised form if the scope increases or life safety improvements are descoped, or stated use changes.  Requester should submit a revised form if scope or use otherwise decreases such that classification(s) may have gone down.  Revised determinations may also be made by the C/S/A Team during design review as “C” comments.

Final determinations are documented by the final, LBO-approved design.  Please print except for signature.

CSA Team Leader Preliminary Determinations

The CSA TL will involve other disciplines as appropriate in making determinations and communicate any differing opinion and its basis to the Requester by email.  If not accepted, then the LBO Deputy for Design Review (ES-EPD GL) will resolve, involving others as appropriate.

| ❐Accept ❐ Accept with Modification: |
| --- |
| Optional Comments/Determinations (e.g., key requirements triggered -- accessibility per IEBC, lateral bracing per IBC 1613.1, R&D equipment anchorage, seismic retrofit per ICSSC RP 8, etc.): |
| Name | Z Number | Signature | Date |

Final Determination by LBO or Deputy if Appealed (n/a if not required)

| ❐Accept CSA Team Determination ❐ Accept with Modification: |
| --- |
| Name | Z Number | Signature | Date |

Once the determinations are made, CSA TL returns to Requester.  The completed form should be retained by the project as a record.

DEFINITIONS, PC/RC/NDC CATEGORIES, AND IEBC TRIGGERED-WORK OVERVIEW

(need not print with form; not part of record)

Repair

Definition: The restoration to good or sound condition of any part of an existing building for the purpose of its maintenance.  Repair includes the patching or restoration or replacement of damaged materials, elements, equipment or fixtures for the purpose of maintaining such components in good or sound condition with respect to existing loads or performance requirements. Limited to work on the item and does not include complete or substantial replacement or other new work (a majority of the original remains). Repairs shall not include the cutting away of any wall, partition, or portion thereof, the removal or cutting of any structural beam or load-bearing support, or the removal or change of any required means of egress or rearrangement of parts of a structure affecting the egress requirements; nor shall ordinary repairs include addition to, alteration of, replacement, or relocation of any standpipe, water supply, sewer, drainage, drain leader, gas, soil, waste, vent, or similar piping, electric wiring, or mechanical or other work affecting public health or general safety.

Work on non-damaged components that is necessary for the required repair of damaged components shall be considered part of the repair and shall generally not be subject to the other classification requirements (must describe in SOW; subject to LBO concurrence).

Level 1 alterations include the removal and replacement or the covering of existing materials, elements, equipment, or fixtures using new materials, elements, equipment, or fixtures that serve the same purpose.  Must follow IEBC Ch. 6.

Level 2 alterations include the reconfiguration of space, the addition or elimination of any door or window, the reconfiguration or extension of any system, or the installation of any additional equipment.  Must follow IEBC Ch. 6 and 7.

Level 3 alterations apply when a major building renovation or reconfiguration work area exceeds 50 percent of the aggregate area of the building.  Must follow IEBC Ch. 6-8.

Work Area. That portion or portions of a building consisting of all altered spaces as indicated on the construction documents.  Work area excludes other portions of the building where incidental work entailed by the intended work must be performed and portions of the building where work not initially intended by the owner is specifically required by code.  Applies to altered spaces, not systems.

Change of Occupancy. A change in the purpose or level of activity within a building that involves a change in the application of requirements of the code including referenced codes.  E.g., adding people or hazardous chemicals must be analyzed for impact.  Must follow IEBC Ch. 9.

Addition. An extension or increase in floor area, number of stories, or height of a building or structure.  Must follow IEBC Ch. 10.

Historic Building.  (at time of writing, LANL has a few at or near S-Site).  Any building or structure that is listed in the State or National Register of Historic Places (ROHP); designated as a historic property under local or state designation law or survey; certified as a contributing resource within a National Register listed or locally designated historic district; or with an opinion or certification that the property is eligible to be listed on the National or State ROHP either individually or as a contributing building to a historic district by the State Historic Preservation Officer or the Keeper of the National ROHP.  Must follow IEBC Ch. 11.

Relocated buildings provisions shall apply to

relocated or moved buildings, including trailers.

Technically Infeasible. An alteration of a building or a facility that has little likelihood of being accomplished because the existing structural conditions require the removal or alteration of a load-bearing member that is an essential part of the structural frame or because other existing physical or site constraints prohibit modification or addition of elements, spaces, or features that are in full and strict compliance with the minimum requirements for new construction and that are necessary to provide accessibility.

NOTE:  In addition to work triggered by IEBC categories, the Int’l Energy Conservation Code mandates envelope upgrades at times (e.g., change of occupancy, conditioning unconditioned space), as does IEBC Ch 3.  See IECC 101.4 and ESM Ch. 14.

Determining PC category of a building (not system or component) from FIMS (Guidance)

- Go to LANL Homepage, & click on More Tools at the bottom of Top Tools.

- On the Top Tools page, select ARCHIBUS WEB Central, & click on Guest Sign In.

- Click on Facility Information, then FIMS, & then FIMS Common Data Elements Console.

- Type TA-Bldg No (i.e., _ _ - _ _ _ _) under Structure Code, & then click Filter.

- Move the scroll bar approx. ¾ of the way across the screen, until you see/read Seismic Essential.

- You will see P_ (e.g., P1, P2, etc.) under Seismic Essential, which means the building structure is PC-_ (i.e., whatever the number is following “P”).

NOTES:

- The Performance Category (PC) of the building structure is not necessarily the same as the PC of the systems & components inside of it.

- What appears in FIMS is JUST the PC for a given structure.

- CMMS Screen D031 may have equipment PC data (field:  “Seismic”).  If not, ESM Chapter 5 Section I details how to determine SDCs for structures, systems & components (SSCs).

- FIMS had not been modified to capture new RC/NDC terminology vice PC at time of writing.

ESM Chapter 5 Section I includes crosswalks from PC-to-RC or NDC.  Consult with FDAR to resolve any NPH determination issues.

IEBC REPAIR AND ALTERATION TRIGGERED-WORK OVERVIEW/GUIDANCE

Note:  Refer to IEBC (and LANL amendments in IBC-GEN Att. B) for actual requirements. Table does not address changes in level of use or occupancy, nor additions; see IEBC Ch. 10 and 11 respectively.

General:   Work can never make the building less safe or less conforming with IBC.  Any Alteration work area must left accessible per IEBC 705 unless technically infeasible (see all definitions above).  Dangerous structural conditions must be rendered safe (ref. IEBC Ch. 2 definition, etc.).

| Building Element or System being Repaired or Altered | Repairs Chapter 6 | Level 1 Alterations Chapter 7 | Level 2 Alterations Chapter 8 | Level 3 Alterations Chapter 9 |
| --- | --- | --- | --- | --- |
|  | Planned work | Triggered Work | Planned Work | Triggered Work | Planned work | Triggered Work | Planned work | Triggered Work |
| Building Elements and Materials | Using like material when originally code-compliant | None, but if needed use like materials, then use ESM-compliant ones. Must replace broken glass with safety glazing in hazardous locations (602.3) | New work or interior finish work | Finishes and new work meet ESM, IBC, and other applicable building codes (fuel gas per 702.6.1) Accessibility improvements (see General note above, probably rarely triggered) When reroofing: parapet and wall anchor work | Alteration per definition above | Comply with Ch 8 (accessibility, etc.) Additional mods in work area or beyond work area may be required (see 703-4; when work area affects 2+ tenants, egress per 805) When reroofing: parapet and wall anchor work Wiring upgrades in A-1, -2, -5, and H (808.2) Ventilation (809) UPC plumbing fixture count when 20% demand increase (810) | Alteration per definition above | Comply with IEBC Ch. 6 & 7 (including 703-5 in work areas in all cases). Additional mods in work area or beyond work area may also be required (see 803-5) |
| Means of Egress | Maintaining level of protection | none | replacement materials and methods maintaining level of protection | Accessibility (see General note above) | Reconfiguration of egress spaces | Improvements in work area, floor, or building per above | Reconfiguration of egress spaces | Improvements in work area, floor, or building per above |
| Accessibility | Maintaining level of protection | none | See Building Elements and Materials above | Accessibility (see General note above) | Accessibility work resulting from a Level 1 Alt | None; just meet Ch 7. If adding a stair, must include accessible route | Accessibility work resulting from a Level 1 Alt | None; just meet IEBC Ch 6. |
| Structural | Using like material | none, but work due to damage must be per 606.2 | Replacement of equipment or roofing which are dead loads (on structure), other reroofing, | See IEBC 707 Always: accessibility (see General note above) | New gravity loads and snow drift effect (cumulative) | See IEBC 807 if 5% or more stress increase | New gravity loads | See 907 |
|  |  |  |  |  | New lateral loads | See 807.5 | Lateral-force-resisting systems: see 907 |
|  |  |  |  |  | Voluntary Improvement of seismic-force-resisting system (those per IEBC App A permitted) | No less conforming or worse irregularities, new and relocated elements per ESM Ch. 5 |  |  |
| Fire protection systems (alarm, suppression) | Using like material and maintaining level of protection | none | See Building Elements and Materials above | See Building Elements and Materials above | Reconfiguration or extension of a system, or installation of a new system | See Building Elements and Materials above | Reconfiguration or extension of a system, or installation of a new system | See Building Elements and Materials above |
| Electrical, Mechanical, and Plumbing | Using like material | None, except E: Certain receptacle and grounding upgrades required M: Forced draft ventilation for fuel-burning appliances where desired/needed P: Materials per UPC |  |  |  |  |  |  |
| Energy Conservation | Meet IECC C504 | New elements/materials in work area must meet IECC C503 | Same as Level 1 + envelope upgrades if conditioning formerly unconditioned per IECC C503 | Same as Level 1, but also see ESM Ch. 14 for possible additional requirements for major renovations |

Chapter/Section references are to IEBC-2015 unless noted otherwise (e.g., ESM).  Table provided for overall understanding only; refer to and comply with IEBC (and IECC for energy conservation) as amended by LANL for all work scope determinations vice this table.

# Footnotes

For demand/capacity ratio, there’s a 10%-latitude-exception for lateral-force-resisting systems with the 10% latitude to be considered cumulatively over the life of the building; see IEBC-2015 807.5 Exception last sentence.

Major mod: Change to a nuclear facility that substantially changes the existing safety basis [adaptation of DOE-STD-1189-2008].  Determination is made through a checklist (see SBP114-1, Safety Basis Development for Projects, Att 2)  Major mods must meet DOE O 420.1C.  Other mods may qualify for code of record design per ESM Ch 1 Section Z10 and IBC-GEN Att B (LEBC).