SECTION 01 5705

TEMPORARY CONTROLS AND COMPLIANCE REQUIREMENTS

*************************************************************************************************************

LANL MASTER SPECIFICATION

Word file at http://engstandards.lanl.gov

This template must be edited for each project.  In doing so, specifier must add job-specific requirements.  Brackets are used in the text to indicate designer choices or locations where text must be supplied by the designer.  Once the choice is made or text supplied, remove the brackets.  The specifications must also be edited to delete specification requirements for processes, items, or designs that are not included in the project -- and specifier’s notes such as these.    To seek a variance from requirements in the specifications that are applicable, contact the Engineering Standards Manual (ESM) Civil POC. Please contact POC with suggestions for improvement as well.

When assembling a specification package, include applicable specifications from all Divisions, especially Division 1, General requirements.

Specification developed for ML-4 projects.  For ML-1, 2, and 3 applications, additional requirements and independent reviews should be added if increased confidence in procurement or execution is desired; see ESM Chapter 1, Section Z10 Specifications and Quality sections.

This section may reference other sections that are future LANL Masters.  Until they exist, the design agency shall either delete these anticipatory references or create a project spec on the topic (whichever is more appropriate for the project).

*************************************************************************************************************

PART 1 	GENERAL

SECTION INCLUDES

Erosion and Sediment Control

Storm Water Management

Site Stabilization

Spill Control and Response

Debris Control

Air Quality

Dust Suppression

Rodent Control

Environmental Restoration Sites

Hazardous Waste

Traffic Control

Water Discharge

Grading, Excavating and Trenching

Washout, Potholing, Directional Drilling

ACTION SUBMITTALS

Submit the following in accordance with project submittal procedures.

For projects operating under a National Pollutant Discharge Elimination System (NPDES) Construction General Permit:

Submit all requested information for the Storm Water Pollution Prevention (SWPP) Plan within 14 days after award of the contract. Submit information in sufficient format and detail as may be required by LANL for completion of the SWPP Plan, including the calculations required by the New Mexico Environmental Department (NMED) Surface Water Quality Bureau (SWQB) state certification of the NPDES Construction General Permit.   The completed SWPPP Plan shall be certified by both LANL and a responsible corporate officer of the Subcontractor prior to the Notice of Intent (NOI) submittal.

Submit the NOI to the United States Environmental Protection Agency (EPA) at least 14 days prior to start of any construction activities.

- Any earth-disturbing or pollutant generating activities shall not begin until at least 14 days after the EPA has acknowledged receipt of the complete NOI on their website at http://ofmpub.epa.gov/CGPSearch/faces/CGPPublicSearch.jspx?_afrLoop=12492164959615666&_afrWindowMode=0&_adf.ctrl-state=k9gsu0fxb_4 and has identified the permit status as “Active”.

- Submit such additional information to and otherwise cooperate and work with LANL to maintain/modify the SWPP Plan throughout the duration of this contract.

Following a review and approval by LANL, submit a Notice of Termination (NOT) to the EPA within 30 days after final stabilization of the site.  Transfer of the site before final stabilization may be negotiated through LANL prior to termination of the Subcontract.

New Mexico Environment Department Notice of Intent (NMED NOI)

The LANL Subcontract Technical Representative (STR) will contact the LANL Environmental Compliance Programs Group (ENV-CP) at 667-0666 prior to the Subcontractor using fertilizer, hydraulically applied mulches, dust suppression additives, soil stabilizers, washouts, potholing fluids, directional drilling fluids, and other substances that are applied to the ground. ENV-CP will determine whether the substances will require a Notice of Intent (NOI) to Discharge be submitted to the New Mexico Environment Department (NMED). Provide information as necessary to obtain the NMED NOI.

Traffic Control Plan

Submit a temporary traffic control plan and subsequent proposed changes to the plan to the LANL STR who will coordinate with the LANL Traffic Engineer for review and approval.

PRODUCTS

Not Used

EXECUTION

  - Erosion and Sediment Control

Properly install Best Management Practices (BMPs) as shown on the drawings or identified in the SWPP Plan, prior to any earth disturbing activity.

Install perimeter sediment controls around disturbed areas and all soil stockpiles and implement controls as necessary to minimize sediment track-out onto streets, sidewalks, and other paved areas.

Maintain BMPs in accordance with SWPP Plan, manufacturer’s recommendations, and the LANL Storm Water Best Management Practices Manual.

When practical, implement permanent BMPs during the construction phase to meet the objectives of temporary sediment and erosion controls.

Disturb only the minimum amount of soil necessary and preserve native topsoil on site unless infeasible.  Give special attention to protecting established vegetation.

Storm Water Management

*************************************************************************************************************

Refer to the ESM Civil Chapter, G10 Site Preparation, for Storm Water Management design requirements.

*************************************************************************************************************

Provide methods to control surface water as identified in the Drawings or SWPP Plan to prevent damage to the Project, the site, and in adjoining areas.

Use permanent storm water management controls (such as detention ponds, riprap, rock check dams, etc.) during the construction in place of temporary storm water management controls whenever practical.

Ensure temporary and permanent storm water management controls are properly installed per Drawings and the SWPP Plan.  Maintain controls per Drawings, the SWPP Plan, and manufacturer’s installation recommendations.

site stabilization

Stabilize all disturbed areas with permanent stabilization measures.  Do not leave any disturbed areas as barren soil.  Final stabilization shall be accepted by LANL Utilities and Institutional Facilities (U&I) and ENV-CP.   The LANL STR will contact LANL U&I storm water system engineer and ENV-CP at 667-0666 to schedule the final walk down and acceptance.

For seeded areas, establish an evenly distributed native perennial vegetative cover with no large bare areas and an average density of 70% of the native background vegetative cover for the area.  Refer to Section 32 9219 Seeding. Begin stabilizing disturbed areas immediately after construction activities have finally or temporarily ended in the area.

If permanent stabilization is impracticable due to seasonal conditions then temporary stabilization measures shall be utilized.

Do not apply fertilizer, hydraulically applied mulches, or soil stabilizers in watercourses.

Spill control and response

In the event of a spill, immediately notify the LANL STR who will contact LANL Emergency Operations (EO).  The Subcontractor is responsible for remediation of any spill.

Store all fuels, lubricants, chemicals, material stockpiles, construction materials, waste material, and other potential pollutants in a designated area on-site.  Provide controls including secondary containment, covering, or leak-proof containers to prevent discharges of pollutant and to minimize contact with storm water. When aboveground petroleum storage capacity is greater than 1,320 gallons (including all equipment and containers 55 gallons or larger), notify the LANL STR who will contact ENV-CP at 667-0666 to initiate the development of a Spill Prevention Control and Countermeasure (SPCC) Plan.

When an aboveground petroleum storage tank (AST) is being constructed with a storage capacity greater than 1,320 gallons and less than 55,000 gallons, submit information in sufficient format and detail as required by LANL for completion of the tank registration, and State notification.  The AST system must be registered with New Mexico Environment Department – Petroleum Storage Tank Bureau NMED-PTSB prior to being placed in service.  Personnel who install AST systems must be certified by the NMED-PTSB.

The LANL STR will contact ENV-CP (667-0666) at least 60 days prior to performing repairs or modifications to existing AST systems.  If the repair or modification is an emergency repair, notify ENV-CP as soon as possible following the repair.  Personnel who modify or repair AST systems must be certified by the NMED-PTSB.

Installation of underground petroleum storage tanks at LANL is not permitted.

Debris Control & Soils management

Use good housekeeping practices to keep sites free of construction debris and trash.  Provide containers for deposit of debris and trash.

Cover all roll-off bins to prevent storm water contact with its contents and accumulation of storm water in the bin.  Notify STR for guidance on discharge requirements if storm water accumulates in a roll-off bin.

Metal shavings, cuttings, grinding residue or other small metal particles shall be placed in leak-proof containers in a manner as to prevent storm water contact with its contents.

Do not drive or move any vehicle on any public road unless the vehicle is constructed, loaded, secured or covered in a manner that will prevent any of its load from dropping, sifting, leaking, or otherwise escaping (except when purposefully cleaning, maintaining, or sanding for traction).

Securely fasten all load covers to vehicles prior to driving on public roads so that the covering does not come loose or become a hazard to others.

Do not bury construction waste, sanitary waste, or trash on-site.

Do not move soil or other material between Technical Areas (TAs) without first obtaining written approval from the receiving TA.  Material must be clean of all contaminates before movement; all transferred soil must be characterized.

Segregate all materials prior to sending material to the LANL Material Recycle Facility (MRF).  The LANL STR will contact ENV-CP to obtain instruction on required sampling and documentation procedures.  Material shall be clean of all contaminates.

Air quality

The LANL STR will contact the LANL Ecology & Air Quality Group (ENV-ES) prior to the Subcontractor operating portable and stationary fuel burning equipment (e.g., generators, rock crushers, asphalt plants).  Drivable equipment does not require notification of ENV-ES.

The LANL STR will contact ENV-ES if the Subcontractor stores over 500 pounds of chemicals at the site.

Dust suppression

When applying potable water for dust control, ensure compliance with Section 01 3545, Water Discharge Requirements.

Do not add additives to potable water for dust control until receiving approval.  Notify the LANL STR who will contact ENV-CP.  Comply with all conditions specified by ENV-CP and the applicable federal and state agencies.  Apply all liquids in a manner that does not result in runoff.

Do not apply dust suppression additives or other substances in watercourses.

PEST Control

Engage pest-control service to recommend practices to minimize attraction and harboring of rodents, roaches, and other pests and to perform extermination and control procedures at regular intervals so Project will be free of pests and their residues at Substantial Completion. Perform control operations lawfully, using environmentally safe materials

Do not use any pesticide (rodenticide) or herbicides without the written approval of LANL.

environmental restoration site

***********************************************************************************************************

Refer to the Civil Chapter, Section G10 Site Preparation, for environmental restoration design requirements.

***********************************************************************************************************

No storm water runoff or soil disturbance shall be allowed across a Solid Waste Management Units (SWMUs) or Areas of Concern (AOCs) that are identified in the contract documents.

Existing BMPs, including vegetative cover, located at a SWMU or AOC shall not be disturbed without coordination with LANL ADEP: Environmental Programs personnel.

An SWMU or AOC cannot be disturbed without LANL ADEP approval and oversight.  The LANL STR will contact ADEP.  Any worker conducting work within the boundary of a SWMU or AOC must be made aware, by the LANL STR, of the potential contaminants present in soils and other materials at the site and the potential hazards associated with those contaminants.

Any soil or other material removed from a SWMU or AOC boundary and not returned to the point of excavation must be managed, characterized, and disposed of by the Subcontractor in accordance with all applicable LANL waste management requirements including approved Waste Profile forms, waste accumulation areas, etc. If the project causes additional runoff to cross the site, install appropriate sediment & erosion controls prior to construction activities.  Best Management Practices must be in place for all projects prior to the start of any soil disturbing activities to prevent potential contaminant migration.

Hazardous and mixed Waste

Store, treat, and/or dispose of hazardous or mixed wastes in accordance with applicable laws and regulations, and LANL requirements.

Register satellite accumulation areas or less than 90 days storage areas with LANL ENV-CP Group prior to storing, handling, treating, or disposing of hazardous or mixed waste.

Contact the ENV-CP Group for more information on the management of hazardous or mixed waste, New Mexico special waste (such as petroleum contaminated soil, spills, chemical products, asbestos waste, infectious waste, etc.), PCBs, construction and demolition debris, and other types of solid waste.

Traffic control

********************************************************************************************************

Refer to the LANL ESM Civil Chapter 3, Section G2010 Roadways, for traffic consideration design requirements.

*********************************************************************************************************

A temporary traffic control plan shall be prepared by a registered Professional Engineer (PE) who is certified as a Professional Traffic Operations Engineer (PTOE).  The detail shall be appropriate to the complexity of the work project and submit to the LANL Traffic Engineer for review and approval.  The LANL Traffic Engineer shall approve any proposed changes in the temporary traffic control plan.

The temporary traffic control plan shall start in the planning phase and continue through the design, construction, and restoration phases.  The temporary traffic control plans and devices shall follow the principles set forth in the MUTCD, latest addition.  Temporary traffic control plans may deviate from the typical applications described in the MUTCD based upon engineering judgment, to allow for conditions and requirements of a particular site.

The temporary Traffic Control Plan shall address the safety of pedestrians and bicycles by providing an alternate, safe route.

Traffic control devices shall be properly maintained during the project, including periodic cleaning and replacement of damaged devices.  Inspection and maintenance of traffic control devices shall be in accordance with NMDOT Standard Specifications for Highway and Bridge Construction Section 618 – Traffic Control Management and performed by personnel certified through ATSSA, ACNM, or IMSA.

Water discharge

Follow Section 01 3545, Water Discharge Requirements.

Grading, excavating, and trenching

Follow Section 31 2000, for Earth Moving requirements.

3.14  	Washout, Potholing, Directional Drilling

- Do not discharge substances to the ground until an NOI has been obtained.  Once a substance is approved by NMED, follow all conditions of the NOI.  Discharges must be documented to the LANL Water Quality Group.

- Washout shall pertain to any generation of wastewater from the washout and/or cleanout of concrete, stucco, paint, form release oil, curing compounds, or other related construction materials.

- Washout will be performed within a leak-proof container or leak-proof pit designed so that no overflows can occur due to inadequate sizing or precipitation. Properly dispose of all hardened excess materials.   Washout areas cannot be placed in or on SWMU or AOC areas, watercourses, Treatment Storage Disposal Facilities, or storm water drainages.

- Liquids from potholing activities must be placed within a defined area within the project site limits surrounded by a Triangular Silt DikeTM, compacted earth berm, or other appropriate control, until the liquids evaporate. Properly dispose of solids. Do not discharge polypropylene glycol, propylene glycol, ethylene glycol, or any other anti-freeze substance without contacting LANL to ensure all environmental requirements have been met. Potholing material may not be removed from the site.

- Directional-drilling mud must be placed within a lined retention pond until the liquids evaporate or properly disposed of. Mud from drilling operations involving a SWMU or AOC must first be evaluated for contaminates before disposal occurs.  Contact ENV-CP at 667-0666 for additional guidance.

END OF SECTION

****************************************************************

Do not delete the following reference information:

****************************************************************

THE FOLLOWING REFERENCE IS FOR LANL USE ONLY

This project specification is based on LANL Master Specification 01 5705, Rev. 5, dated February 25, 2015.