SECTION 06 2000

FINISH CARPENTRY

*************************************************************************************************************

LANL MASTER SPECIFICATION

This template must be edited for each project.  In doing so, specifier must add job-specific requirements.  Brackets are used in the text to indicate designer choices or locations where text must be supplied by the designer.  Once the choice is made or text supplied, remove the brackets.  The specifications must also be edited to delete specification requirements for processes, items, or designs that are not included in the project -- and specifier’s notes such as these.  To seek a variance from requirements in the specifications that are applicable, contact the Engineering Standards Manual Architectural POC. Please contact POC with suggestions for improvement as well.

When assembling a specification package, include applicable specifications from all Divisions, especially Division 1, General requirements.

Specification developed for ML-4 projects.  For ML-1, 2, and 3 applications, additional requirements and independent reviews should be added if increased confidence in procurement or execution is desired; see ESM Ch 1 Section Z10 Specifications and Quality Sections.

*************************************************************************************************************

PART 1  GENERAL

1.1	SECTION INCLUDES

A.	Finish carpentry items

B.	Hardware and attachment installation

C.	Wood trim and moldings installation

D.	Job-built shelving and cabinets

  - REFERENCES

A.	The following documents, including others referenced herein, form a part of this Specification to the extent designated:

- Architectural Woodwork Institute (AWI)

Architectural Woodwork Quality Standards, Guide Specifications and Quality Certification Program

2.   American National Standards Institute/Builders Hardware Manufacturers Association (ANSI/BHMA)

ANSI/BHMA A156.9	Cabinet Hardware

ANSI/BHMA A156.18	Materials and Finishes

3. 	National Electrical Manufacturers Association (NEMA)

NEMA GP50, for horizontal surfaces

NEMA GP28, for vertical surfaces

NEMA LD-3 BK20, backing sheet

1.3	SUBMITTALS

- Submit the following in accordance with Section 01 3300, Submittal Procedures.

1.	Shop drawings of architectural woodwork indicating component profiles, fastening methods, jointing details, and accessories at a minimum scale of 1 1/2 inch equals one foot.

2. 	Catalog data for hardware and specialty items.

1.4	QUALITY ASSURANCE

- Provide materials and perform work in accordance with above referenced documents.

1.5	PROJECT CONDITIONS

A.	Protect materials and work from moisture damage.

B.	Sequence installation to ensure utility connections are achieved in an orderly and expeditious manner.

C.	Coordinate the work with plumbing, electrical rough-in and installation of associated components.

PART 2  PRODUCTS

2.1	LUMBER MATERIALS

A.	Softwood lumber: PS 20, AWI Custom grade, average moisture content of 4-9 percent.

B.	Hardwood lumber: NHLA:  AWI Custom grade, average moisture content of 4-9 percent, vertical grain, suitable for transparent finish.

2.2	PANEL PRODUCTS

A.	Softwood plywood: PS 1, AWI Custom grade, with particleboard core material.

B.	Hardwood plywood: AWI Custom grade, with particleboard core and red oak face veneer.

C.	Particleboard: AWI standard Medium density with Type 1 water-resistant adhesive, of grade to suit application, sanded faces.

D.	Hardboard: Standard grade, untempered, smooth one side.

2.3	OVERLAYS – HIGH PRESSURE LAMINATES

A.	Plastic laminate: [NEMA GP50, 0.050 inch thick, for horizontal surfaces] [NEMA GP28, 0.028 inch thick, for vertical surfaces], matte finish faces.

B.	Backing sheet: NEMA LD-3 BK20, 0.020 inch thick, undecorated sheet.

C.	Adhesives (non-toxic, formaldehyde free) as recommended by plastic laminate manufacturer.

2.4	ACCESSORIES

A.	Plastic laminate self-edge trim on plastic laminate faced panels.

B.	Matching wood veneer tape on hardwood faced panels.

C.	Plastic edge trim; extruded flat shape, smooth surface finish, self locking serrated tongue, of width to match panel, color as selected, on painted softwood panels.

D.	Clear, heat strengthened, 1/4 inch safety glass for wall cabinet doors.

E.	Fasteners of size and type to suit application.

- Concealed joint fasteners of threaded steel.

  - HARDWARE

A.	Cabinet and casework hardware to conform to ANSI/BHMA A156.9, Grade 1.  Hardware finishes as designated in ANSI/BHMA A156.18.

2.6.	FABRICATION

A.	Fabricate products to AWI Custom grade standards for [Reveal Overlay] [Flush Overlay] [Exposed Face Frame] design.

B.	When necessary to cut and fit, provide materials with ample allowance for cutting. Provide trim, if required, for scribing and cutting.

C.	Apply plastic laminate finish in full, uninterrupted sheets consistent with manufactured sizes.  Fit corners and joints hairline; secure with concealed fasteners.

D.	Apply plastic laminate backing sheet to reverse side of plastic laminate finished surfaces.

- Apply self-edging to exposed panel edges.

F.	Casework and cabinet hardware to be furnished by the casework/cabinet manufacturer.

2.7.	SHOP FINISHING OF WOOD FACED CABINETS

A.	Painted finish: Apply 1 coat of primer and 2 coats of semi-gloss acrylic latex enamel as specified in Section 09 9100, Painting.

B.	Natural finish: Apply sanding sealer, stain and 2 coats of satin polyurethane as specified in Section 09 9100, Painting.

PART 3  EXECUTION

3.1	INSPECTION

A.	Verify adequacy of backing and support framing.

B.	Set and secure materials and components in place, plumb and level.

C.	Verify mechanical, electrical and building items affecting work of this Section are in place and ready to receive this work.

3.2	INSTALLATION

A.	Set and secure materials and components in place, plumb and level.

- Carefully scribe work abutting other components, with maximum gaps of 1/32 inch.  Do not use additional overlay trim to conceal larger gaps.

3.3	ERECTION TOLERANCES

A.	Maximum variation from true position is 1/16 inch.

B.	Maximum offset from true alignment with abutting materials is 1/32 inch.

END OF SECTION

*****************************************************************

Do not delete the following reference information:

*****************************************************************

FOR LANL USE ONLY

This project specification is based on LANL Master Specification 06 2000, Rev. 1, dated May 1, 2008.