SECTION 06 2000

FINISH CARPENTRY

*************************************************************************************************************

LANL MASTER SPECIFICATION

This template must be edited for each project.  In doing so, specifier must add job-specific requirements.  Brackets are used in the text to indicate designer choices or locations where text must be supplied by the designer.  Once the choice is made or text supplied, remove the brackets.  The specifications must also be edited to delete specification requirements for processes, items, or designs that are not included in the project — and specifiers’ notes such as these.  Additional tailoring requirements are contained in ESM Chapter 1 Section Z10 Att. F, Specifications.

To seek a variance from requirements in the specifications that are applicable, contact the Engineering Standards Manual Architectural POC. Please contact POC with suggestions for improvement as well.

When assembling a specification package, include applicable specifications from all Divisions, especially Division 1, General requirements.

Specification developed for ML-4 projects.  For ML-1, 2, and 3 applications, additional requirements and independent reviews should be added if increased confidence in procurement or execution is desired; see ESM Ch 1 Section Z10 Specifications and Quality Sections.

*************************************************************************************************************

PART 1  GENERAL

  - SECTION INCLUDES

- Finish carpentry items

- Hardware and attachment installation

- Wood trim and moldings installation

- Job-built shelving and cabinets

  - REFERENCES

*************************************************************************************************************

Edit the references to include only those that apply to the edited specification section.

*************************************************************************************************************

- The following documents, including others referenced herein, form a part of this Specification to the extent designated:

- Architectural Woodwork Institute (AWI)

  - Architectural Woodwork Standards

- [American National Standards Institute/Builders Hardware Manufacturers Association (ANSI/BHMA)

  - ANSI/BHMA A156.9	Cabinet Hardware

  - ANSI/BHMA A156.18	Materials and Finishes]

- American National Standards Institute/Hardware, Plywood and Veneer Association (ANSI/HPVA)

  - ANSI/HPVA HP-1 American National Standard for Hardwood & Decorative Plywood

- Bay Area Air Quality Management District (AQMD)

  - AQMD Reg. 8, Rule 51

- California Air Resources Board (CARB)

- California Department of Public Health

  - Standard Practice for the Testing of Volatile Organic Emissions from Various Sources Using Small-Scale Environmental Chambers

- Forest Stewardship Council: FSC Guidelines – Forest Stewardship Council Guidelines

- Green Seal: GS-36 – Aerosol Adhesives

- National Electrical Manufacturers Association (NEMA)

  - NEMA  LD 3 High Pressure Decorative Laminates

- National Hardwood Lumber Association

  - NHLA Grading Rules for North American Hardwoods

- National Institute of Standards and Technology (NIST)

  - Voluntary Product Standard PS 20

- South Coast Air Quality Management District: SCAQMD

  - Rule 1168 – Adhesive and Sealant Applications

- Toxic Substances Control Act (1976)

  - Subchapter VI – Formaldehyde Standards for Composite Wood Products (2016)

- US Green Building Council (USGBC)

  - Maximum VOC Concentration Levels: USGBC LEED BD+C New Construction Indoor Air Quality Assessment credit

*************************************************************************************************************

Edit submittals to include only those absolutely necessary to assure requirements and features that are important for the specific project will be met.

*************************************************************************************************************

  - SUBMITTALS

- Submit the following in accordance with Section 01 3300, Submittal Procedures.

- Shop drawings of architectural woodwork indicating component profiles, fastening methods, jointing details, and accessories at a minimum scale of 1 1/2 inch equals one foot.

- Catalog data for hardware and specialty items.

*************************************************************************************************************

Include only sustainable design submittals that are appropriate for the project’s sustainable design goals, if any.

*************************************************************************************************************

- [Sustainable Design Submittals

      - Chain-of-custody certificates indicating that products specified to be made from certified wood, softwood lumber and hardwood lumber, comply with forest certification requirements. Include documentation that manufacturer is certified for chain of custody by an FSC-accredited certification body. Include statement indicating cost for each certified wood product.

        - Forest Stewardship Council (FSC): Provide letter of certification signed by lumber supplier. Indicate compliance with FSC “Principled for Natural Forest Management” and identify certifying organization.

        - Submit FSC certification numbers; identify each certified product on a line-item basis.

*************************************************************************************************************

Green building rating systems typically include credit for sustainably harvested wood. USGBC-LEED™, for example, includes credit for use of sustainably harvested wood certified under Forest Stewardship Council Guidelines.  Under LEED™ v3, a minimum of 50 percent of wood-based materials and products incorporated into the Project must be certified in accordance with the Forest Stewardship Council Guidelines. Under LEED™ v4, products meeting wood products criteria are valued at 100% of their cost for the purposes of credit achievement calculation.

*************************************************************************************************************

      - Engineered Wood Products: Provide documentation that composite wood and agrifiber products are in compliance with the Toxic Substances Control Act (1976)’s amendment from of 2016, Subchapter VI – Formaldehyde Standards for Composite Wood Products

      - Product Data for adhesives, documentation including printed statement of VOC content.

        - For Aerosol Adhesives: Submit Green Seal Certification to GS-36 and description of the basis of certification.

        - For Adhesives and Sealants: Submit manufacturer’s certification that products comply with SCAQMD Rule 1168 in areas where exposure to freeze/thaw conditions and direct exposure to moisture will not occur. In areas where freeze/thaw conditions do exist or direct exposure to moisture can occur, submit manufacturer’s certification that products comply with Bay Area AQMD Reg. 8, Rule 51 for containers larger than 16 oz and with California Air Resources Board (CARB) for containers 16 oz or less.

*************************************************************************************************************

Green building rating systems may include credit for low emitting materials. USGBC-LEED™ v3, for example, includes credits for low-emitting materials, including:  adhesives and sealants, paints and coatings, carpets, and composite wood and agrifiber products.  Under LEED™ v4, adhesives and sealants are to comply with California’s South Coast Air Quality Management District (SCAQMD) #1168 and aerosol adhesives are to comply with Green Seal GS-36.

*************************************************************************************************************

      - Product data for recycled content

        - Engineered Wood Products

          - Indicate recycled content; indicate percentage of pre-consumer and post-consumer recycled content per unit of product.

*************************************************************************************************************

LEED grants one credit to a project for using materials with recycled content that is the sum of postconsumer recycled content plus one-half the preconsumer recycled content, based on cost.

Green Globes US also provides points for reused building materials and components and for building materials with recycled content.

*************************************************************************************************************

      - Product data for USDA BioPreferred Products: Indicate percentage of biobased content in the following products:

        - Adhesives

          - Description: Solvent products formulated for use in removing asbestos, carpet, and tile mastics as well as adhesive materials, including glue, tape, and gum, from various surface types.

          - Recommended Biobased Content: 58% minimum.

        - Composite Panels

          - Acoustical Panels

            - Description: Engineered products designed for use as structural and sound deadening material suitable for office partitions and doors.

            - Recommended Biobased Content: 37% minimum.

          - Countertops

            - Description: Engineered products designed to serve as horizontal work surfaces in locations such as kitchens, break rooms or other food preparation areas, bathrooms or lavatories, and workrooms

            - Recommended Biobased Content: 89% minimum.

          - Interior Panels

            - Description: Engineered products designed specifically for interior applications and providing a surface that is impact-, scratch-, and wear-resistant and that does not absorb or retain moisture.

            - Recommended Biobased Content: 55% minimum.

          - Plastic Lumber

            - Description: Engineered products suitable for non-structural outdoor needs such as exterior signs, trash can holders, and dimensional letters.

            - Recommended Biobased Content: 23% minimum.

- Laboratory Test Reports for [adhesives] [and] [composite-wood products], documentation indicating that products comply with the testing and product requirements of the California Department of Health Services’ “Standard Practice for the Testing of Volatile Organic Emissions from Various Sources Using Small-Scale Environmental Chambers.”

  - QUALITY ASSURANCE

  - Provide materials and perform work in accordance with above referenced documents.

  - [Sustainable Design Requirements

- Certified Wood Materials: Furnish softwood lumber and hardwood lumber wood materials certified in accordance with FSC Guidelines.

- Recovered Content Materials: Furnish materials with recovered content for:

- Required: Particleboard/fiberboard component must be 80-100% recovered wood or wood composite.

- Preferred: 100% recovered agricultural fiber.

- VOC emissions:  Provide low VOC products.

- Adhesives and sealants:  Comply with California’s South Coast Air Quality Management District (SCAQMD) #1168 or with Bay Area AQMD Reg. 8, Rule 51 for containers larger than 16 oz and with California Air Resources Board (CARB) for containers 16 oz or less.

- Aerosol adhesives:  Comply with Green Seal GS-36.

- Engineered Wood Products:

- Formaldehyde compliance with the Toxic Substances Control Act (1976)’s amendment from 2016, Subchapter VI – Formaldehyde Standards for Composite Wood Products.

- VOC emission compliance with the US Green Building Council’s Maximum VOC Concentration Levels outlined in the USGBC LEED BD+C New Construction Indoor Air Quality Assessment credit.]

  - PROJECT CONDITIONS

  - Protect materials and work from moisture damage.

  - Sequence installation to ensure utility connections are achieved in an orderly and expeditious manner.

  - Coordinate the work with plumbing, electrical rough-in and installation of associated components.

PART 2  PRODUCTS

  - LUMBER MATERIALS

  - Softwood lumber: NIST PS 20, AWI Custom grade, average moisture content of 4-9 percent.

  - Hardwood lumber: NHLA:  AWI Custom grade, average moisture content of 4-9 percent, vertical grain, suitable for transparent finish.

  - PANEL PRODUCTS

  - Softwood plywood: NIST PS 1, AWI Custom grade, with particleboard core material.

  - Hardwood plywood: ANSI/HPVA HP-1, AWI Custom grade, with particleboard core and red oak face veneer.

  - Particleboard: AWI standard Medium density with moisture-resistant adhesive, of grade to suit application, sanded faces.

  - Hardboard: Standard grade, untempered, smooth one side.

  - OVERLAYS – HIGH PRESSURE DECORATIVE LAMINATES

    - Plastic laminate: [NEMA LD 3, General Purpose, HGS 0.048 inch thick, for horizontal surfaces], VGS 0.028 inch thick, for vertical surfaces], [VGL 0.020 inch thick, for backing sheet], matte finish faces.

    - Adhesives (non-toxic, formaldehyde-free) as recommended by plastic laminate manufacturer.

  - ACCESSORIES

    - Plastic laminate self-edge trim on plastic laminate faced panels.

    - Matching wood veneer tape on hardwood faced panels.

    - Plastic edge trim; extruded flat shape, smooth surface finish, self locking serrated tongue, of width to match panel, color as selected, on painted softwood panels.

    - Clear, heat-strengthened, 1/4-inch safety glass for wall cabinet doors.

- Fasteners of size and type to suit application.

- Concealed joint fasteners of threaded steel.

  - [HARDWARE

  - Cabinet and casework hardware to conform to ANSI/BHMA A156.9, Grade 1.  Hardware finishes as designated in ANSI/BHMA A156.18.]

  - FABRICATION

      - Fabricate products to AWI Custom grade standards for Face Frame cabinets with [Overlay] [Inset] [Partial Overlay] doors] [Frameless cabinets with [Overlay] [Inset] doors] design.

      - When necessary to cut and fit, provide materials with ample allowance for cutting. Provide trim, if required, for scribing and cutting.

      - Apply plastic laminate finish in full, uninterrupted sheets consistent with manufactured sizes.  Fit corners and joints hairline; secure with concealed fasteners.

- Apply plastic laminate backing sheet to reverse side of plastic laminate finished surfaces.

- Apply self-edging to exposed panel edges.

- Casework and cabinet hardware to be furnished by the casework/cabinet manufacturer.

  - SHOP-FINISHING OF WOOD-FACED CABINETS

- Painted finish: Apply 1 coat of primer and 2 coats of semi-gloss acrylic latex enamel as specified in Section 09 9100, Painting.

- Natural finish: Apply sanding sealer, stain and 2 coats of satin polyurethane as specified in Section 09 9100, Painting.

PART 3  EXECUTION

  - INSPECTION

- Verify adequacy of backing and support framing.

- Set and secure materials and components in place, plumb and level.

- Verify mechanical, electrical and building items affecting work of this Section are in place and ready to receive this work.

  - INSTALLATION

- Set and secure materials and components in place, plumb and level.

- Carefully scribe work abutting other components, with maximum gaps of 1/32 inch.  Do not use additional overlay trim to conceal larger gaps.

  - ERECTION TOLERANCES

- Maximum variation from true position is 1/16 inch.

- Maximum offset from true alignment with abutting materials is 1/32 inch.

END OF SECTION

*****************************************************************

Do not delete the following reference information:

*****************************************************************

THE FOLLOWING REFERENCE IS FOR LANL USE ONLY

This project specification is based on LANL Master Specification 06 2000, Rev. 2, dated February 8, 2017.