SECTION 08 1400

WOOD DOORS

*************************************************************************************************************

LANL MASTER SPECIFICATION SECTION

Word file at https://engstandards.lanl.gov/specs.shtml

Rev. 5 Summary of Changes Updated references and other minor changes.

This template must be edited for each project.  In doing so, specifier must add job-specific requirements.  Brackets are used in the text to indicate designer choices or locations where text must be supplied by the designer.  Once the choice is made or text supplied, remove the brackets.  The document must also be edited to delete requirements for processes, items, or designs that are not included in the project - and specifiers’ notes such as these.  Additional tailoring requirements are contained in ESM Chapter 1 Section Z10 Att. F, Specifications.

To seek a variance from requirements that are applicable, contact the Engineering Standards Manual Architectural POC. Please contact POC with suggestions for improvement as well.

When assembling a specification package, include applicable sections from all Divisions, especially Division 1, General requirements.

Section developed for ML-4 projects.  For ML-1, 2, and 3 applications, additional requirements and independent reviews should be added if increased confidence in procurement or execution is desired; see ESM Chapter 1 Section Z10 Specifications and Quality sections.
*************************************************************************************************************

PART 1 GENERAL

  - SECTION INCLUDES

- Flush wood doors, [fire-rated and non-fire rated]

*************************************************************************************************************

Edit the references to include only those that apply to the edited specification section.

*************************************************************************************************************

  - REFERENCES

- The following documents, including others referenced herein, form a part of this Specification to the extent designated:

- Architectural Woodwork Institute (AWI)

  - AWI - Architectural Woodwork Standards 2nd Edition published jointly by Architectural Woodwork Institute (AWI), the Architectural Woodwork Manufacturers Association of Canada (AWMAC), and the Woodwork Institute (WI).

- Bay Area Air Quality Management District (AQMD)

  - AQMD Reg. 8, Rule 51

- California Air Resources Board (CARB)

- California Department of Health Services

  - Standard Practice for the Testing of Volatile Organic Emissions from Various Sources Using Small-Scale Environmental Chambers

- Forest Stewardship Council: FSC Guidelines – Forest Stewardship Council Guidelines

- Green Seal: GS-36 – Commercial Adhesives

- National Fire Protection Association (NFPA)

  - NFPA 80 - Standard for Fire Doors and Other Opening Protectives

  - NFPA 252 - Standard Methods of Fire Tests of Door Assemblies

- South Coast Air Quality Management District: SCAQMD

  - Rule 1168 – Adhesive and Sealant Applications

- Toxic Substances Control Act (1976)

  - Title VI – Formaldehyde Standards for Composite Wood Products (2010)

- United States Department of Agriculture (USDA) BioPreferred Program

- US Green Building Council (USGBC)

  - Maximum VOC Concentration Levels: USGBC LEED BD+CL New Construction Indoor Air Quality Assessment credit

- Window And Door Manufacturers Association (WDMA)

  - WDMA I.S.1A:  "Industry Standard for Wood Flush Doors"

*************************************************************************************************************

Edit submittals to include only those absolutely necessary to assure requirements and features that are important for the specific project will be met.

*************************************************************************************************************

  - SUBMITTALS

[Submit the following in accordance with the requirements of Section 01 3300, Submittal Procedures:

- Action/Informational Submittals:

- Catalog data for each type of wood door, including details of core and edge construction, trim for openings, and finishing specifications for doors to receive factory finish.

- Color and finish samples of factory finished doors for approval.

- Shop drawings indicating location, size, and hand of each door, elevation of each kind of door, details of construction, location and extent of hardware blocking, fire ratings, requirements for factory finishing and other pertinent data.

- Warranty as specified.]

*************************************************************************************************************

Include only sustainable design submittals that are appropriate for the project’s sustainable design goals, if any.

*************************************************************************************************************

- [Sustainable Design Submittals

      - Sustainable Design (LD) Submittals:  Comply with requirements specified in [individual specification sections]  Section 01 8113.13 - [LEED v4 and] Guiding Principles 2020: Requirements for water efficiency, energy efficiency, material composition, and indoor air quality requirements

      - Chain-of-custody certificates indicating if products comply with forest certification requirements. Include documentation that manufacturer is certified for chain of custody by an FSC-accredited certification body. Include statement indicating cost for each certified wood product.

        - Forest Stewardship Council (FSC): Provide letter of certification signed by lumber supplier. Indicate compliance with FSC “Principled for Natural Forest Management” and identify certifying organization.

        - Submit FSC certification numbers; identify each certified product on a line-item basis.

*************************************************************************************************************

Green building rating systems typically include credit for sustainably harvested wood. USGBC-LEED™, for example, includes credit for use of sustainably harvested wood certified under Forest Stewardship Council Guidelines.  Under LEED™ v3, a minimum of 50 percent of wood-based materials and products incorporated into the Project must be certified in accordance with the Forest Stewardship Council Guidelines. Under LEED™ v4, products meeting wood products criteria are valued at 100% of their cost for the purposes of credit achievement calculation..  *************************************************************************************************************

      - Product Data for adhesives, documentation including printed statement of VOC content.

        - For Aerosol Adhesives: Submit Green Seal Certification to GS-36 and description of the basis of certification.

        - For Adhesives and Sealants: Submit manufacturer’s certification that products comply with SCAQMD Rule 1168 in areas where exposure to freeze/thaw conditions and direct exposure to moisture will not occur. In areas where freeze/thaw conditions do exist or direct exposure to moisture can occur, submit manufacturer’s certification that products comply with Bay Area AQMD Reg. 8, Rule 51 for containers larger than 16 oz and with California Air Resources Board (CARB) for containers 16 oz or less.

*************************************************************************************************************

Green building rating systems may include credit for low emitting materials. USGBC-LEED™ v3, for example, includes credits for low-emitting materials, including:  adhesives and sealants, paints and coatings, carpets, and composite wood and agrifiber products.  Under LEED™ v4, adhesives and sealants are to comply with California’s South Coast Air Quality Management District (SCAQMD) #1168 and aerosol adhesives are to comply with Green Seal GS-36.

*************************************************************************************************************

      - Product data for USDA BioPreferred Products: Indicate percentage of

        - Adhesives

          - Description: Solvent products formulated for use in removing asbestos, carpet, and tile mastics as well as adhesive materials, including glue, tape, and gum, from various surface types.

          - Recommended Biobased Content: 58%

        - Composite Panels

          - Acoustical Panels

- Description: Engineered products designed for use as structural and sound deadening material suitable for office partitions and doors.

- Recommended Biobased Content: 37%

      - Laboratory Test Reports for [adhesives] [and] [composite-wood products], documentation indicating that products comply with the testing and product requirements of the California Department of Health Services’ “Standard Practice for the Testing of Volatile Organic Emissions from Various Sources Using Small-Scale Environmental Chambers.”.]

  - QUALITY ASSURANCE

  - Quality Standards:  Provide wood flush doors complying with the following standards:

    - WDMA I.S.1A:  "Industry Standard for Wood Flush Doors".

    - AWI Quality Standards: "Architectural Woodwork Standards. Designations for grade and door construction under types of doors refers to this standard.

- Fire-Rated Wood Doors:  Provide wood doors which are identical in materials and construction to units tested in door and frame assemblies per NFPA 252 and which are labeled and listed for ratings indicated by UL, Warnock Hersey or other testing and inspection agency acceptable to Architect.

- Manufacturer:  Obtain doors from a single manufacturer to ensure uniformity in quality of appearance and construction, unless otherwise indicated.

- Provide materials and perform work in accordance with above referenced documents.

- [Sustainable Design Requirements

      - Certified Wood Materials: Furnish wood materials certified in accordance with FSC Guidelines.

      - Recovered Content Materials: Furnish materials with recovered content for:

        - Required: Particleboard/fiberboard component must be 80-100% recovered wood or wood composite

        - Preferred: 100% recovered agricultural fiber

      - VOC emissions:  Provide low VOC products.

        - Adhesives and sealants:  Comply with California’s South Coast Air Quality Management District (SCAQMD) #1168 or with Bay Area AQMD Reg. 8, Rule 51 for containers larger than 16 oz and with California Air Resources Board (CARB) for containers 16 oz or less.

        - Aerosol adhesives:  Comply with Green Seal GS-36

        - Engineered Wood Products:

          - Formaldehyde compliance with the Toxic Substances Control Act (1976)’s amendment from January of 2010, Title VI – Formaldehyde Standards for Composite Wood Products

          - VOC emission compliance with the US Green Building Council’s Maximum VOC Concentration Levels outlined in the USGBC LEED BD+CL New Construction Indoor Air Quality Assessment credit]

  - PRODUCT DELIVERY, STORAGE, AND HANDLING

- Protect wood doors during transit, storage, and handling to prevent damage, staining, soiling and deterioration.  Comply with requirements of WDMA I.S.1.A Standard as well as with manufacturer's instructions.  Package doors at factory prior to shipping using manufacturer's standard method.

- Identify each door with individual opening numbers which correlate with designation system used on shop drawings for door, frames, and hardware, using temporary, removable, or concealed markings.

  - SPECIFIC PRODUCT WARRANTY

- Door Manufacturer's Warranty:  Submit written agreement on door manufacturer's standard form signed by manufacturer, installer, and Subcontractor, agreeing to repair or replace defective doors which have warped (bow, cup, or twist) or which show telegraphing of core construction in face veneers, or do not conform to tolerance limitations of WDMA and AWI.

- Warranty (to become effective after date of final acceptance):

  - Ten years for solid core flush interior doors.

- Replace doors where Subcontractor's work contributed to rejection or to voiding of manufacturer's warranty.

PART 2 PRODUCTS

  - MANUFACTURERS

- Timberland Door

- Eggers Industries

- Assa Abloy Doors

- Mohawk Doors

- Marshfield DoorSystems

  - INTERIOR FLUSH WOOD DOORS

- Solid Core Doors with Wood Veneer Faces:  Comply with the following requirements:

  - Faces:  1/8-inch, 3-ply panel, [plain sliced, [Premium] [Custom] grade, red oak veneer].

  - Finish:  AWI System TR-4.

  - Core Construction:  PC-HPDL (Particleboard core).

- Fire-Rated Solid Core Doors:  Comply with the following requirements.

  - Faces and AWI Grade:  Provide faces and grades to match non-rated doors in same area of building.

  - Construction:  Manufacturer's standard core construction as required to provide fire-resistance indicated.

  - Edge Construction:  Provide manufacturer's standard edge construction for improved screw-holding capability and split resistance. Do not use edges composed of a single layer of treated lumber.

  - LIGHT FRAMES

- Frames for Light Openings in Fire Doors:  Manufacturer's standard frame formed of 18 gauge cold-rolled steel, factory-primed, and approved for use in door of fire-rating indicated.

  - GENERAL FABRICATION REQUIREMENTS

- Openings:  Cut and trim openings through doors and panels as shown. Comply with applicable requirements of referenced standards for kind(s) of doors required.

  - Light Openings:  Factory cut openings. Trim openings for non-fire-rated doors with solid wood moldings.

  - REFITTING AND PREPARATION FOR HARDWARE

- Comply with tolerance requirements of AWI for pre-fitting.  Machine doors for hardware requiring cutting of doors.  Comply with final hardware schedules and door frame shop drawings and with hardware templates and other essential information required to ensure proper fit of doors and hardware.

  - Take accurate field measurements of hardware mortises in metal frames to verify dimensions and alignment before proceeding with machining in factory.

PART 3  EXECUTION

  - INSPECTION

- Examine door frames, after their installation, and doors, prior to their hanging, as follows:

  - Verify that frames comply with indicated requirements for type, size, location, and swing characteristics and have been installed with plumb jambs and level heads.

  - Verify that doors are free of defects that could cause their rejection.

  - INSTALLATION

- Condition doors to average prevailing humidity in installation area prior to hanging.

- Manufacturer's Instructions:  Install wood doors to comply with manufacturer's instructions and of referenced AWI standard and as indicated.

  - Install fire-rated doors in corresponding fire-rated frames in accordance with requirements of NFPA 80.

- Job-fit Doors:  Align and fit doors in frames with uniform clearances and bevels as indicated below.  Machine doors for hardware.  Seal cut surfaces after fitting and machining.

  - Fitting Clearances:  For non-rated doors provide clearances of 1/8 in. at jambs and heads; 1/16 in. per leaf at meeting stiles for pairs of doors; and 1/8 in. from bottom of door to top of decorative floor finish or covering.

              - For fire-rated doors, provide clearances complying with NFPA 80.

            - Bevel non-rated doors: 1/8-in. in 2-in. at lock edges.

            - Bevel fire-rated doors 1/8-in. in 2-in. at lock edges.

- Pre-fit Doors:  Fit to frames and machine for hardware to whatever extent not previously worked at factory as required for fit and uniform clearance at each edge.

  - ADJUSTMENT AND PROTECTION

- Operation:  Rehang or replace doors which do not swing or operate freely, as directed by Architect.

- Finished Doors:  Refinish or replace doors damaged during installation, as directed by Architect.

- Institute protective measures as recommended and accepted by door manufacturer to assure that wood doors will be without damage or deterioration at time of final acceptance.

end of section

***********************************************************

Do not delete the following reference information:

***********************************************************

THE FOLLOWING STATEMENT IS FOR LANL USE ONLY

This project specification section is based on LANL Master Specification Section 08 1400 Rev. 5, dated December 14, 2022.