SECTION 11 1313

LOADING DOCK BUMPERS

*************************************************************************************************************

LANL MASTER SPECIFICATION

This template must be edited for each project.  In doing so, specifier must add job-specific requirements.  Brackets are used in the text to indicate designer choices or locations where text must be supplied by the designer.  Once the choice is made or text supplied, remove the brackets.  The specifications must also be edited to delete specification requirements for processes, items, or designs that are not included in the project -- and specifier’s notes such as these.  To seek a variance from requirements in the specifications that are applicable, contact the Engineering Standards Manual Architectural POC. Please contact POC with suggestions for improvement as well.

When assembling a specification package, include applicable specifications from all Divisions, especially Division 1, General requirements.

Specification developed for ML-4 projects.  For ML-1, 2, and 3 applications, additional requirements and independent reviews should be added if increased confidence in procurement or execution is desired; see ESM Chapter 1 Section Z10 Specifications and Quality sections.
*************************************************************************************************************

PART 1  GENERAL

1.1	SECTION INCLUDES

A.	Dock bumpers of reinforced rubber with attachment frames.

1.2	SUBMITTALS

A.	Submit the following in accordance with requirements of Section 01 3300.

1.	Catalog data indicating unit dimensions, details of construction, description of materials and method of anchorage.

2.	Manufacturer’s installation instructions.

PART 2  PRODUCTS

2.1	MANUFACTURERS

A.	Durable Corporation, Dura-Dock

2.2	COMPONENTS

A.	Use bumpers made of reinforced rubber pads, ozone resistant, laminated and compressed in position with two galvanized steel rods with threaded ends, washers and nuts; between galvanized steel angle end plates.

1.	Projection from dock face:  6 inches

2.	Vertical height:  10 inches

3.	Length:  24 inches

4.	Profile:  rectangular

B.	Use galvanized 3/4 inch expansion bolts to anchor units to face of dock.

PART 3  EXECUTION

3.1	INSPECTION

A.	Verify that anchor bolt placement is acceptable.

3.2	INSTALLATION

A.	Install in accordance with manufacturer’s installation instructions.

B.	Secure end frames to concrete.

END OF SECTION

*****************************************************************

Do not delete the following reference information:

*****************************************************************

FOR LANL USE ONLY

This project specification is based on LANL Master Specification 11 1313 Rev. 1, dated May 19, 2008.