SECTION 05 3113

STEEL FLOOR DECKING

****************************************************************************************************

LANL MASTER SPECIFICATION

When editing to suit project, author shall add job-specific requirements and delete only those portions that in no way apply to the activity (e.g., a component that does not apply).  To seek a variance from applicable requirements, contact the ESM Structural POC.

When assembling a specification package, include applicable specifications from all Divisions, especially Division 1, General Requirements.

Delete information within “stars” during editing.

Specification developed for ML-3 projects.  For ML-1 / ML-2, additional requirements and QA reviews are required.

****************************************************************************************************PART 1 GENERAL

  - SECTION INCLUDES

- Steel floor deck system.

  - DESIGN REQUIREMENTS

- Design steel roof deck in accordance with SDI Design Manual for Composite Decks, Form Decks, and Roof Decks.

  - SUBMITTALS

- Submit the following in accordance with Section 01 3300, Submittal Procedures:

  - Certificates of compliance for:

    - Steel deck.

    - Sheet metal for ancillary materials.

    - Self-drilling, self-tapping screws (mechanical fasteners).

    - Welders, in accordance in with AWS D1.1 for welders who will perform field welding.

  - Shop drawings including the following information:

    - Materials furnished including accessories.

    - Splices and connections.

    - Erection plan.

  - Catalog data for:

    - Metal deck.

    - Self-drilling, self tapping screws (mechanical fasteners).

    - Touch-up paint.

  - Test data and design calculations to provide documentation of performance for mechanical fasteners.

  - QUALITY ASSURANCE

- Conform to SDI Design Manual for Composite Decks, Form Decks, and Roof Decks.

  - DELIVERY, STORAGE, AND HANDLING

- Deliver, store, and handle metal roof deck:

  - With equipment of adequate capacity.

  - Without overstressing or permanently damaging material.

  - Without damaging finish.

- Deliver manufactured materials in original unopened packages, containers, or bundles with manufacturers' label intact and legible.

- Store all materials off the ground, under cover and away from damp surfaces.

- Remove damaged, unlabeled, or unsatisfactory material which does not meet this specification from the job site.

PART 2 PRODUCTS

  - MATERIALS

- Steel Deck

  - Provide sheet steel, for deck which is required to be galvanized, conforming to ASTM A446, Grade [ A ], [ C ], or [ E ], with a minimum yield strength of 
Fy = 33,000 psi with G90 galvanized coating conforming to ASTM A525.

  - Provide sheet steel, for deck which is required to be painted, conforming to ASTM A611, Grade [ C ], or [ D ], with a minimum yield strength of 
Fy = 33,000 psi.

  - Deck type, profile and section properties are shown on the Drawings. The information stated establishes minimum acceptable values. Alternate sections, profiles and/or designs may be submitted for approval.

  - Provide venting slots in deck to receive light weight insulating concrete.

- Acoustic Steel Deck

  - Provide a composite acoustic deck with a NRC of [ 0.70 ] when tested in accordance with ASTM C432, [ 20 ] gage sheet steel with G90 galvanized coating conforming to ASTM A525, [ 1 1/2 ] inches deep, perforated with manufacturer’s standard holes. Deck type, profile, and section properties are shown on the drawings. The information stated establishes minimum acceptable values. Alternative sections, profiles and/or designs may be submitted for review.

- Primer

  - Provide primer and touch-up primer conforming to SSPC 15, Type 1, red oxide, for nongalvanized surfaces.

  - Provide touch-up primer conforming to SSPC 20, Type 1, inorganic, for galvanized surfaces.

- Welding Materials

  - Provide welding electrodes complying with the requirements of AWS D1.3.

  - Provide [ 14 ] gage weld washers where required.

- Mechanical Fasteners

  - Provide Number [ 12 ] Tek Fasteners by ITW Builder, Itasca, Illinois with ultimate capacities equal to or greater than the following values:

    - Pullout in [ 3/16 ] inch thick steel: [ 3400 ] pounds.

    - Shear, fastening [ 20 ] gage steel to [ 20 ] gauge steel: [ 750 ] pounds.

    - Force to pull [ 20 ] gage steel over head of fastener: [ 1400 ] pounds.

- Accessories

  - Provide steel accessories that are a standard item of the steel deck manufacturer fabricated with steel of the same type and finish as the deck.

  - Provide manufacturer's standard flute closure of closed cell foam rubber, 
1 inch thick, to fit selected deck profile.

  - FABRICATION

- Shop fabricate decking and accessories to exact lengths and shapes.

- Fabricate deck sheets to be formed identically and so each sheet registers smoothly with adjacent sheets.

PART 3 EXECUTION

  - INSTALLATION

- Erect metal decking in accordance with SDI Design Manual for Composite Decks, Form Decks, and Roof Decks.

- Erect metal decking in accordance with the approved erection drawing and in accordance with the manufacturer's instructions.

- Welding

  - Perform all welding in accordance with AWS D1.3.

  - Provide weld washers for deck in accordance with manufacturer’s requirements.

  - Weld in accordance with the diaphragm requirements stated on the Drawings.

  - Avoid burning through the deck while field welding to supports.

- Mechanical Fasteners

  - Install connections with mechanical fasteners in accordance with the manufacturer's instructions and the approved erection drawings.

- Provide 1 1/2 inch minimum bearing on steel support members. Align and level on supports.

- Provide 4 inch minimum bearing on masonry support members. Align and level on supports.

- Reinforce all holes that interrupt more than 1 rib.

- Install all accessories shown on the approved erection drawings.

- Weld shear stud connectors through steel deck to structural members below.

- Install concrete stops at floor edges and openings.

- Seal deck joints, lap ends, and penetrations with sealant.

  - CLEAN-UP AND FINISH TOUCH-UP

- After erection, remove weld spatter, grease and oil from decking.

- Immediately after welding deck in place, touch-up welds, burned areas, and surface coating damage. Use prime paint specified in Part 2.

END OF SECTION

************************************************************

Do not delete the following reference information:

************************************************************

FOR LANL USE ONLY

This project specification is based on LANL Master Specification 05 3113 Rev. 0, dated January 6, 2006.