SECTION 06 4100

ARCHITECTURAL WOOD CASEWORK

*************************************************************************************************************

LANL MASTER SPECIFICATION SECTION

Word file at https://engstandards.lanl.gov

Rev. 3 Summary of Changes: Updated references and other minor changes.

This template must be edited for each project.  In doing so, specifier must add job-specific requirements.  Brackets are used in the text to indicate designer choices or locations where text must be supplied by the designer.  Once the choice is made or text supplied, remove the brackets.  The specifications must also be edited to delete specification requirements for processes, items, or designs that are not included in the project — and specifiers’ notes such as these.  Additional tailoring requirements are contained in ESM Chapter 1 Section Z10 Att. F, Specifications.

To seek a variance from requirements in the specifications that are applicable, contact the Engineering Standards Manual Architectural POC. Please contact POC with suggestions for improvement as well.

When assembling a specification package, include applicable specifications from all Divisions, especially Division 1, General requirements.

Specification developed for ML-4 projects.  For ML-1, 2, and 3 applications, additional requirements and independent reviews should be added if increased confidence in procurement or execution is desired; see ESM Ch 1 Section Z10 Specifications and Quality Sections.

*************************************************************************************************************

PART 1  GENERAL

  - SECTION INCLUDES

- Custom fabricated cabinet units

- Countertops

- Miscellaneous wood shelving

  - REFERENCES

*************************************************************************************************************

Edit the references to include only those that apply to the edited specification section.

*************************************************************************************************************

- The following documents, including others referenced herein, form a part of this Specification to the extent designated:

      - Architectural Woodwork Institute (AWI)

        - Architectural Woodwork Standards

      - American National Standards Institute/Builders Hardware Manufacturers Association (ANSI/BHMA)

- ANSI/BHMA A156.9	Cabinet Hardware

- ANSI-BHMA A156.18	Materials and Finishes

- American National Standards Institute/Hardware, Plywood and Veneer Association (ANSI/HPVA)

        - ANSI/HPVA HP-1 American National Standard for Hardwood & Decorative Plywood

- Bay Area Air Quality Management District (AQMD)

              - AQMD Reg. 8, Rule 51

- California Air Resources Board (CARB)

- California Department of Public Health

- Standard Practice for the Testing of Volatile Organic Emissions from Various Sources Using Small-Scale Environmental Chambers

- Forest Stewardship Council: FSC Guidelines – Forest Stewardship Council Guidelines

- Green Seal: GS-36 – Aerosol Adhesives

- National Electrical Manufacturers Association (NEMA)

- NEMA LD 3 High Pressure Decorative Laminates

- National Hardwood Lumber Association

- NHLA Grading Rules for North American Hardwoods

- National Institute of Standards and Technology (NIST)

- Voluntary Product Standard PS 1, PS 20

- South Coast Air Quality Management District: SCAQMD

- Rule 1168 – Adhesive and Sealant Applications

- Toxic Substances Control Act (1976)

- Subchapter VI – Formaldehyde Standards for Composite Wood Products (2016)

- US Green Building Council (USGBC)

- Maximum VOC Concentration Levels: USGBC LEED BD+C New Construction Indoor Air Quality Assessment credit.

*************************************************************************************************************

Edit submittals to include only those absolutely necessary to assure requirements and features that are important for the specific project will be met.

*************************************************************************************************************

  - [SUBMITTALS

- Submit the following in accordance with Section 01 3300, Submittal Procedures:

- Shop drawings of architectural woodwork indicating component profiles, fastening methods, joining details, and accessories at a minimum scale of 1 1/2 inch equals one foot.

- Catalog data for hardware and specialty items.]

*************************************************************************************************************

Include only sustainable design submittals that are appropriate for the project’s sustainable design goals, if any.

*************************************************************************************************************

- [Sustainable Design Submittals

      - Sustainable Design (LD) Submittals:  Comply with requirements specified in [individual specification sections]  Section 01 8113.13 - [LEED v4 and] Guiding Principles 2020: Requirements for water efficiency, energy efficiency, material composition, and indoor air quality requirements

      - Chain-of-custody certificates indicating that products specified to be made from certified wood, softwood lumber and hardwood lumber, comply with forest certification requirements. Include documentation that manufacturer is certified for chain of custody by an FSC-accredited certification body. Include statement indicating cost for each certified wood product.

        - Forest Stewardship Council (FSC): Provide letter of certification signed by lumber supplier. Indicate compliance with FSC “Principles for Natural Forest Management” and identify certifying organization.

        - Submit FSC certification numbers; identify each certified product on a line-item basis.

*************************************************************************************************************

Green building rating systems typically include credit for sustainably harvested wood. USGBC-LEED™, for example, includes credit for use of sustainably harvested wood certified under Forest Stewardship Council Guidelines.  Under LEED™ v3, a minimum of 50 percent of wood-based materials and products incorporated into the Project must be certified in accordance with the Forest Stewardship Council Guidelines. Under LEED™ v4, products meeting wood products criteria are valued at 100% of their cost for the purposes of credit achievement calculation.

*************************************************************************************************************

      - Engineered Wood Products: Provide documentation that composite wood and agrifiber products are in compliance with the Toxic Substances Control Act (1976)’s amendment from  2016, Subchapter VI – Formaldehyde Standards for Composite Wood Products

      - Product Data for adhesives, documentation including printed statement of VOC content.

        - For Aerosol Adhesives: Submit Green Seal Certification to GS-36 and description of the basis of certification.

        - For Adhesives and Sealants: Submit manufacturer’s certification that products comply with SCAQMD Rule 1168 in areas where exposure to freeze/thaw conditions and direct exposure to moisture will not occur. In areas where freeze/thaw conditions do exist or direct exposure to moisture can occur, submit manufacturer’s certification that products comply with Bay Area AQMD Reg. 8, Rule 51 for containers larger than 16 oz and with California Air Resources Board (CARB) for containers 16 oz or less.

*************************************************************************************************************

Green building rating systems may include credit for low emitting materials. USGBC-LEED™ v3, for example, includes credits for low-emitting materials, including:  adhesives and sealants, paints and coatings, carpets, and composite wood and agrifiber products.  Under LEED™ v4, adhesives and sealants are to comply with California’s South Coast Air Quality Management District (SCAQMD) #1168 and aerosol adhesives are to comply with Green Seal GS-36.

*************************************************************************************************************

      - Product data for recycled content

        - Engineered Wood Products

          - Indicate recycled content; indicate percentage of pre-consumer and post-consumer recycled content per unit of product

*************************************************************************************************************

LEED grants one credit to a project for using materials with recycled content that is the sum of postconsumer recycled content plus one-half the preconsumer recycled content, based on cost.

Green Globes US also provides points for reused building materials and components and for building materials with recycled content.

*************************************************************************************************************

      - Product data for USDA BioPreferred Products: Indicate percentage of biobased content in the following products:

        - Adhesives

          - Description: Solvent products formulated for use in removing asbestos, carpet, and tile mastics as well as adhesive materials, including glue, tape, and gum, from various surface types.

          - Recommended Biobased Content: 58%

        - Composite Panels

          - Countertops

            - Description: Engineered products designed to serve as horizontal work surfaces in locations such as kitchens, break rooms or other food preparation areas, bathrooms or lavatories, and workrooms

            - Recommended Biobased Content: 89%

          - Interior Panels

            - Description: Engineered products designed specifically for interior applications and providing a surface that is impact-, scratch-, and wear-resistant and that does not absorb or retain moisture.

            - Recommended Biobased Content: 55%

- Laboratory Test Reports for [adhesives] [and] [composite-wood products], documentation indicating that products comply with the testing and product requirements of the California Department of Health Services’ “Standard Practice for the Testing of Volatile Organic Emissions from Various Sources Using Small-Scale Environmental Chambers.”.]

  - QUALITY ASSURANCE

- Provide materials and perform work in accordance with above referenced documents.

- Sustainable Design Requirements

      - Certified Wood Materials: Furnish softwood lumber and hardwood lumber wood materials certified in accordance with FSC Guidelines.

      - Recovered Content Materials: Furnish materials with recovered content for:

        - Required: Particleboard/fiberboard component must be 80-100% recovered wood or wood composite

        - Preferred: 100% recovered agricultural fiber

      - VOC emissions:  Provide low VOC products.

        - Adhesives and sealants:  Comply with California’s South Coast Air Quality Management District (SCAQMD) #1168 or with Bay Area AQMD Reg. 8, Rule 51 for containers larger than 16 oz and with California Air Resources Board (CARB) for containers 16 oz or less.

        - Aerosol adhesives:  Comply with Green Seal GS-36

        - Engineered Wood Products:

          - Formaldehyde compliance with the Toxic Substances Control Act (1976)’s amendment from 2016, Subchapter VI – Formaldehyde Standards for Composite Wood Products

          - VOC emission compliance with the US Green Building Council’s Maximum VOC Concentration Levels outlined in the USGBC LEED BD+C New Construction Indoor Air Quality Assessment credit

  - DELIVERY, STORAGE AND HANDLING

  - Protect woodwork during transit, delivery, storage and handling to prevent damage, soiling and deterioration.

  - Do not deliver casework until painting, wet work and similar operations that could damage casework have been completed in installation areas.  If casework must be stored in other than installation areas, store only in areas meeting requirements for installation areas.

  - PROJECT CONDITIONS

  - Do not install casework until required temperature and relative humidity have been stabilized, and will be maintained in installation areas in accordance with AWI instructions.

PART 2  PRODUCTS

  - LUMBER MATERIALS

*************************************************************************************************************

If cabinetwork is to have a painted finish, softwood is the logical material. Hardwood is the best for natural finishes.

*************************************************************************************************************

- Softwood lumber:  NIST PS 20, AWI Custom grade; average moisture content of 4-9 percent.

OR

- Hardwood lumber: NHLA, AWI Custom grade; average moisture content of 4-9 percent; vertical grain suitable for transparent finish.

  - PANEL PRODUCTS

- Softwood plywood: NIST PS 1, AWI Custom grade, with particleboard core material.

- Hardwood plywood: ANSI/HPVA HP-1, AWI Custom grade, with particleboard core material and red oak face veneer.

- Particleboard: AWI standard, medium density, with Type 1 moisture resistant adhesive; of grade to suit application; sanded faces.

- Hardboard: Standard grade, untempered smooth one side.

  - OVERLAYS – HIGH PRESSURE LAMINATES

  - Plastic laminate: [NEMA LD 3 General Purpose, HGS 0.048 inch thick, for horizontal surfaces VGS 0.28 inch for vertical surfaces] matte finish faces.

  - Adhesives (non-toxic, formaldehyde free) as recommended by plastic laminate manufacturer.

  - ACCESSORIES

  - Plastic laminate self-edge trim on plastic laminate faced panels.

  - Matching wood veneer tape on hardwood faced panels.

  - Plastic edge trim; extruded flat shape, smooth surface finish, self locking serrated tongue, of width to match panel, color as selected, on painted softwood panels.

  - Clear, heat strengthened, 1/4 inch tempered glass for glazed wall cabinet doors.

  - Fasteners of size and type to suit application.

- Concealed joint fasteners of threaded steel.

  - HARDWARE

  - Cabinet and casework hardware to conform to ANSI/BHMA A156.19, Grade 1.  Hardware finishes as designated in ANSI/BHMA A156.18.

  - Shelf standards: Formed steel channels, cut for support brackets at 1-inch centers, satin chrome finish.

  - Support brackets: Steel brackets formed to fit slots in standards, for nominal 12-inch shelves, satin chrome finish.

  - Drawer and door pulls: Recessed, satin chrome steel.

  - Cabinet locks: Keyed cylinder, two keys per lock, steel with polished chrome finish.

  - Door catches: Magnetic type.

  - Drawer slides: Galvanized steel with ball bearings separating tracks, full extension type.

  - Hinges: Fully concealed type.

  - FABRICATION

  - Fabricate products to AWI Custom grade standards for Face Frame cabinets with [Overlay] [Inset] [Partial Overlay] doors] [Frameless cabinets with [Overlay] [Inset] doors] design.

  - Comply with requirements of referenced quality standard for moisture content of lumber at time of fabrication, and for humidity conditions in the installation area.

  - Before fabricating casework, obtain field measurements and verify dimensions and shop drawing details as required for accurate fit to other work.

  - Fabricate casework to dimensions, profiles and details indicated.  Provide openings and mortises precut, where possible, to receive hardware, other items and other work. Locate openings accurately, using templates or roughing-in diagrams for proper size and shape. Smooth edges of cutoffs and, where located in countertops and similar exposures, seal edges of cutouts with a water resistant coating.

  - Ease edges to 1/16 inch radius at corners of cabinets and edges of solid wood (lumber) members less than 1-inch in nominal thickness, 1/8-inch radius for edges of rails and similar members over 1-inch in nominal thickness.

  - Finish shelves, doors, and exposed edges with appropriate edging, wood veneer tape, plastic laminate or plastic extrusion. Use one piece for full length only.

  - Door and drawer fronts: 3/4 inch thick.

  - Apply plastic laminate finish in full, uninterrupted sheets, consistent with manufactured sizes.  Fit corners and joints hairline, secure with concealed fasteners.

  - Apply laminate backing sheet to reverse sides of plastic laminate faced surfaces.

  - Complete fabrication, assembly, finishing, hardware installation, and other work before shipment to project site to maximum extent possible. Disassemble components only as necessary for shipment and installation. Where necessary for fitting at site, provide ample allowance for scribing, trimming and fitting.

  - Shop assemble casework for delivery to site in units easily handled and to permit passage through building openings.

  - Casework and cabinet hardware shall be furnished by the casework/cabinet manufacturer.

  - FINISHES

*************************************************************************************************************

  - Painted finish: One coat of primer, 2 coats of semi-gloss latex acrylic enamel as specified in Section 09 9100.

OR

  - Natural finish: Sanding sealer, stain and 2 coats of satin polyurethane as specified in Section 09 9100.

*************************************************************************************************************

PART 3  EXECUTION

  - INSPECTION

  - Verify presence and accuracy of backing and support framing.

  - Verify locations and sizes of utility rough-ins associated with casework.

  - INSTALLATION

  - Set and secure casework in place, rigid, plumb and level.

  - Use fixture attachments in concealed locations for wall mounted components.

  - Use concealed joint fasteners to align and secure adjoining cabinet units and countertops.

  - Carefully scribe and cut casework abutting other Work, with gaps of 1/32 inch maximum. Do not use additional overlay trim for this purpose.

  - Secure cabinets to floor using appropriate angles and fasteners.

  - ADJUSTING

  - Adjust moving or operating parts to function smoothly and correctly.

  - CLEANING

  - Clean casework, counters, shelves, hardware, fittings and fixtures.

END OF SECTION

*****************************************************************

Do not delete the following reference information:

*****************************************************************

THE FOLLOWING REFERENCE IS FOR LANL USE ONLY

This project specification is based on LANL Master Specification 06 4100, Rev. 3, dated December 12, 2022.