SECTION 09 2116

GYPSUM BOARD SYSTEMS SECTION

*************************************************************************************************************

LANL MASTER SPECIFICATION

Word file at https://engstandards.lanl.gov

Rev. 8 Summary of Changes Minor changes including sustainable design references.

Sustainable design:  This Section includes reference to SD that only applies to certain larger projects (e.g., Total Estimated Cost > $5 million) and other projects having SD goals (ref. ESM Ch. 14).  Delete if not applicable.

This template must be edited for each project.  In doing so, specifier must add job-specific requirements.  Brackets are used in the text to indicate designer choices or locations where text must be supplied by the designer.  Once the choice is made or text supplied, remove the brackets.  Template must also be edited to delete specification requirements for processes, items, or designs that are not included in the project, add requirements not contained herein as well as deleting specifier’s notes such as these.  To seek a variance from requirements that are applicable, contact the Engineering Standards Manual Architectural POC. Please contact POC with suggestions for improvement as well.

When assembling a specification package, include applicable sections from all Divisions, especially Division 01, General requirements.

Section developed for ML-4 projects.  For ML-1, 2, and 3 applications, additional requirements and independent reviews should be added if increased confidence in procurement or execution is desired; see ESM Chapter 1 Section Z10 Specifications and Quality sections.

Structural/seismic

Suspended gypsum board ceiling applications in accordance with (IAW) this section, and surrounded by and connected to walls or soffits that are laterally braced to the structure above, need not comply with the seismic sway-bracing requirements of ASCE 7 Chapter 13, paragraph 13.5.6 (per Exception 2).

Interior partitions that are of height < 9-ft., and of linear weight < 10 lbs x partition height, and subjected to a horizontal seismic load < 5 psf need not be laterally braced (to the building structure) per the exception to ASCE 7 Ch. 13, para. 13.5.8.

For members in a cold-formed steel (CFS)-framed system that are part of the building’s envelope and/or gravity and/or lateral load load-resisting system, Section 05 4000, Cold-Formed Metal Framing, must be used in lieu of this section.

NOTE:  Applications involving CFS nonstructural members that are included in the scope of AISI S220, North American Standard for Cold-Formed Steel Framing – Nonstructural Members must be designed and installed accordingly.  And, on a related note, this section is not to be used for such applications “as-is.”

- An alternative to editing this section for compliance with AISI S220 is to use a commercial guide spec for Section 09 2216, Nonstructural Metal Framing (available from SpecLink, AIA MasterSpec, SpecText, etc.).

*************************************************************************************************************

GENERAL

SECTION INCLUDES

Metal stud wall framing.

Metal channel ceiling framing.

Gypsum board and joint treatment.

Acoustic insulation.

*************************************************************************************************************

Edit the references to include only those that apply to the edited specification section.

*************************************************************************************************************

REFERENCES

ASTM INTERNATIONAL

ASTM C 475 - Standard Specification for Joint Compound and Joint Tape for Finishing Gypsum Board

ASTM C 557 – Standard Specification for Adhesives for Fastening Gypsum Wallboard to Wood Framing

ASTM C 645 – Standard Specification for Nonstructural Steel Framing Members

ASTM C 665 – Standard Specification for Mineral-Fiber Blanket Thermal Insulation for Light Frame Construction and Manufactured Housing

ASTM C 754 - Standard Specification for Installation of Steel Framing Members to Receive Screw-Attached Gypsum Panel Products

ASTM C 840 – Standard Specification for Application and Finishing of Gypsum Board

ASTM C 954 - Standard Specification for Steel Drill Screws for the Application of Gypsum Panel Products or Metal Plaster Bases to Steel Studs from 0.033 in. to 0.112 in. in Thickness

ASTM C 955 - Standard Specification for Cold-Formed Steel Structural Framing Members

ASTM C 1002 – Standard Specification for Steel Self-Piercing Tapping Screws for Application of Gypsum Panel Products or Metal Plaster Bases to Wood Studs or Steel Studs

ASTM C 1047 - Standard Specification for Accessories for Gypsum Wallboard and Gypsum Veneer Base

ASTM C 1396 - Standard Specification for Gypsum Board

Gypsum Association (GA)

GA-214 – Recommended Levels of Gypsum Board Finish

GA-216 – Application and Finishing of Gypsum Panel Products

GA-225 - Repair of Fire-Rated Gypsum Panel Product Systems

GA-600 – Fire Resistance Design Manual

Underwriters Laboratories (UL) – Certifications Directory

*************************************************************************************************************

Edit submittals to include only those absolutely necessary to assure requirements and features that are important for the specific project will be met.

*************************************************************************************************************

ACTION SUBMITTALS

Sustainable Design (LD) Submittals:  Comply with requirements specified in [individual specification sections]  Section [01 8113.13] - [LEED v4 and] Guiding Principles 2020: Requirements for water efficiency, energy efficiency, material composition, and indoor air quality requirements.

Submit the following:

Catalog data on metal framing, gypsum board, joint tape, joint compound and texturing materials.

Gypsum manufacturer’s documentation of recycled content for gypsum board.

Gypsum manufacturer’s documentation of buyback and/or recycling program.

Manufacturer’s written certification that all materials are free of asbestos.

Manufacturer’s installation instructions.

Twelve-inch-square sample of gypsum board with texture finish.

QUALITY ASSURANCE

Perform work in accordance with ASTM C 840, GA-214, GA-216, and GA-600.

REGULATORY REQUIREMENTS

Conform to IBC for fire-rated assemblies as follows:

Fire-Rated Partitions: Listed assembly UL U465 for 1 hour rating, UL U411 for 2-hour rating.

Fire-Rated Ceiling [and Soffits]: Listed assembly UL [  ].

Fire-Rated Shaft Walls: Listed assembly UL [  ].

PRODUCTS

  - MANUFACTURERS

Georgia Pacific Corp.

National Gypsum Company.

United States Gypsum Company.

FRAMING MATERIALS

Studs and Tracks

Minimum Base-Steel Thickness: [As indicated on Drawings] [0.0269 inch] [0.0296 inch] ASTM C 645; [or] [0.0329 inch] ASTM C 645 and ASTM C955.

Depth: [As indicated on Drawings] [3-5/8 inches] [6 inches] [4 inches] [2-1/2 inches] [1-5/8 inches].

Galvanized sheet steel, C shape.

Furring, framing and accessories conforming to ASTM C 645 and GA-600.

Fasteners for Metal Framing: of type, material, size, corrosion resistance, holding power, and other properties required to fasten steel members to substrates.

Adhesive conforming to ASTM C 557 and GA-216.

GYPSUM BOARD MATERIALS

Recycled Content:  Gypsum recycled content to be the greatest amount available, up to 28 percent post-industrial content.  Subject to compliance with requirements, use synthetic (flue-gas) gypsum when available.  Paper facing to be 100 percent post consumer recycled content.  Fiber gypsum board shall consist of recycled newspaper and gypsum over recycled newspaper, gypsum, and perlite core.

Gypsum board conforming to ASTM C 1396, fire resistive, Type X, 5/8-inch thick, maximum practical length, with square cut ends and tapered edges.

Moisture resistant gypsum board conforming to ASTM C 1396, 5/8-inch thick, maximum practical length, with square cut ends and tapered edges.

Gypsum coreboard conforming to ASTM C 1396, 1-inch thick, maximum practical length, with square cut ends and tapered edges.

ACCESSORIES

Acoustic insulation conforming to ASTM C 665, preformed, formaldehyde-free, glass fiber batts, [3 1/2] [5 1/2] [6 1/4] [6 1/2] inches thick, unfaced, friction-fit type.

Fasteners: Steel Drill Screws conforming to ASTM C 1002 unless otherwise indicated.

Use screws complying with ASTM C 954 for fastening panels to steel members from 0.033 to 0.112 inch thick.

For fastening cementitious backer units, use screws of type and size recommended by the panel manufacturer.

Corner beads of metal and paper construction.

Edge bead conforming to ASTM C 1047 and GA-216.

Joint materials conforming to ASTM C 475 and GA-216; reinforcing tape, joint compound, adhesive (all 100 percent asbestos free) and water.

Latex based texture finish materials.

EXECUTION

  - METAL STUD INSTALLATION

Install studs as indicated on the drawings and in accordance with manufacturer’s instructions and ASTM C 754.

Refer to Drawings for locations of studding extending to the ceiling, through the ceiling, and to structure above.

ACOUSTICAL ACCESSORIES INSTALLATION

Refer to Drawings for location of partitions with acoustical treatment.

Install acoustic sealant at joint between gypsum board and floor, and to seal penetrations of partitions by conduit, pipe, ductwork, etc.

Place acoustic insulation between studs, around cut openings, behind and around electrical and mechanical items within or behind partitions, and tight to items passing through partitions.

SHAFT WALL INSTALLATION

Install in accordance with manufacturer’s instructions to GA-600 requirements.

[SUSPENDED CEILING GRILLAGE INSTALLATION

Install grillage in accordance with ASTM C 754.

Suspend 1-1/2 inch furring channels from structural members with 8 gage wires at 48 inches on center, and within 6 inches of walls.

Install furring channels at right angle to channels [at 16 inches on center] using formed clips.]

GYPSUM BOARD INSTALLATION

Install gypsum board in accordance with manufacturer’s instructions.

In non-fire rated partitions, erect single layers of gypsum board in most economical direction, with edges and ends occurring over firm bearing.

In fire rated partitions erect single layer of gypsum board vertically, with edges and ends occurring over firm bearing.

Install screws in accordance with manufacturer’s instructions.

In double layer installations, erect second layer perpendicular to first layer, secured to first layer with adhesive. Offset joints of second layer from joints of first layer.

Treat cut edges and holes in moisture resistant gypsum board with sealant.

Install corner beads at exterior corners.  Install edge trim where gypsum board abuts dissimilar materials.

JOINT TREATMENT

Tape, fill and sand exposed joints, edges, and corners to produce smooth surface, ready for finish.

Feather coats onto adjoining surfaces so that camber is maximum 1/32 inch.

TEXTURE FINISH

Apply finish texture coating to attain a light sand finish.

TOLERANCES

Maximum variation of finished gypsum board surface from true flatness is 1/8 inch in 10 feet in any direction.

END OF SECTION

************************************************************

Do not delete the following reference information:

************************************************************

THE FOLLOWING STATEMENT IS FOR LANL USE ONLY

This project specification section is based on LANL Master Specification 09 2116 Rev. 8, dated August 4, 2022.