SECTION 10 1405

EXTERIOR SIGNAGE

*************************************************************************************************************

LANL MASTER SPECIFICATION SECTION

Word file at https://engstandards.lanl.gov

Rev. 4 Summary of Changes Updated references and other minor changes.

Application of this Section is intended for all new facilities and additions, or enlargements of existing facilities.

Coordinate this Section with Architectural Standard Drawings ST-G2040-4. Use applicable drawing sheets and edit for project specific requirements as needed. Selection of types of signs, text to be included on signs and their resultant sizes, and installation locations is required.

________________________

This section must be edited for each project.  In doing so, specifier must add job-specific requirements.  Brackets are used in the text to indicate specifier’s choices or locations where text must be supplied by the specifier.  Once the choice is made or text supplied, remove the brackets.  The document must also be edited to delete requirements for processes, items, or designs that are not included in the project, adding requirements not contained herein as well as deleting specifier’s notes such as these.  To seek a variance from requirements that are applicable, contact the Engineering Standards Manual Architectural POC. Please contact POC with suggestions for improvement as well.

When assembling a specification package, include applicable sections from all Divisions, especially Division 1, General requirements.

Section developed for ML-4 projects.  For ML-1, 2, and 3 applications, additional requirements and independent reviews should be added if increased confidence in procurement or execution is desired; see ESM Chapter 1 Section Z10 Specifications and Quality sections.

*************************************************************************************************************

PART 1  GENERAL

  - SECTION INCLUDES

- Signs for [facilities,] [technical areas,] [operations and divisions,] [freestanding building identification,] [on building identification (lettering, on building identification - plaques,] [regulatory – safety and security,] [trail and transit,] [interpretive and route markers].

  - REFERENCE STANDARDS

- Americans with Disabilities Act Accessibility Guidelines.

****************************************************************************************************

For signs placed within road right-of-ways:

****************************************************************************************************

- [Manual of Uniform Traffic Control Devices (MUTCD).]

- ASTM International

- ASTM B 209 - Standard Specification for Aluminum and Aluminum-Alloy Sheet and Plate

- ASTM B 221 - Standard Specification for Aluminum and Aluminum-Alloy Extruded Bars, Rods, Wire, Profiles, and Tubes

*************************************************************************************************************

Edit submittals to include only those absolutely necessary to assure requirements and features that are important for the specific project will be met.

*************************************************************************************************************

  - [ACTION / INFORMATIONAL SUBMITTALS

- Product Data: Submit product data for specified products. Include material details for each sign specified. Include printed illustrative literature.

- Sustainable Design (LD) Submittals:  Comply with requirements specified in [individual specification sections]  Section 01 8113.13 - [LEED v4 and] Guiding Principles 2020: Requirements for water efficiency, energy efficiency, material composition, and indoor air quality requirements

- Shop Drawings

- Show layout, profiles, and product components, including dimensions, anchorage, and accessories.

- Refer to the Drawings for locations, quantities, copy and sizes.

- Manufacturer’s Installation Instructions

- Samples - Submit color samples for verification purposes.]

  - [CLOSE OUT SUBMITTALS

- Provide copy of manufacturer’s recommended care and cleaning methods including precautions against harmful cleaning materials and methods.

- Provide copy of manufacturer’s warranty documents.]

  - QUALITY ASSURANCE

- Obtain all products from a single supplier.

- Installation shall be performed by installer specialized and experienced in work similar to that required for this project.

  - DELIVERY, STORAGE, AND HANDLING

- Wrap or otherwise package assemblies for protection against damage and staining.

- Deliver products in manufacturer’s original, unopened, undamaged containers with identification labels intact.

- Store products protected from weather, temperature, and other harmful conditions as recommended by supplier.

- Handle products in accordance with manufacturer’s instructions.

  - WARRANTY

- Provide manufacturer’s standard material and workmanship warranty.

PART 2  PRODUCTS

  - MANUFACTURER

- ASI Signage Innovations, no substitutions accepted.

  - DESCRIPTION

- Free standing panel signs: ASI Compass Series Exterior Panel Sign System

- ID wide post profile.

- Letter style: [Frutiger 75 Black] [and] [or] [Frutiger 95 Ultra Black].

- Graphics to be Vinyl Die Cut and Paint.

- Text to be [white premium 3M vinyl – reflective] [black premium 3M vinyl – reflective] [blue premium 3M vinyl to match Pantone Matching System (PMS) #3025U] [scotchcal bright yellow 3622 vinyl]

- LANL Logo to be painted to match PMS 8240 metallic.

- Building mounted, Flat Cut Out (FCO) Aluminum Letters.

  - MATERIALS

- Aluminum Panels meeting ASTM B209, alloy EN 5052 H12, minimum 0.125” thick.

- Aluminum Extrusions meeting ASTM B221, alloy 6063-T5.

- Provide end caps, couplings, coupling fittings, mounting fittings, interchangeable fittings, and other hardware and accessories necessary for a complete installation.

- FCO Aluminum letters meeting ASTM B209, alloy En 5052 H12, minimum 0.5” thickness.

- Conceal fasteners if possible; otherwise, locate fasteners to appear inconspicuously.

  - FABRICATION

- Comply with requirements indicated on the drawings for materials, thickness, finish, color, design, shapes, sizes, and details of construction.

- Design, fabricate, and install sign assemblies to prevent buckling, opening of joints and over-stressing of welds and fasteners.

- Mill joints to a tight, hairline fit. Form joints exposed to weather to exclude water penetration.

- Pre-assemble signs in the shop to the greatest extent possible to minimize field assembly. Disassemble signs only as necessary for shipping and installation.

- Coordinate dimensions and attachment methods to produce message panels with closely fitting joints. Align edges and surfaces with one another in the relationship indicated.

- Increase material thickness or reinforce with concealed stiffeners of backing materials as required to produce surfaces without distortion, buckles, warp, or other surface deformations.

  - FINISHES

- High temperature cured polyester primer to be 2 mil thick layers for optimum surface coat adhesion and weatherability.

- Topcoat to be two component, water-based, non-toxic, zero VOC, high temperature cured polyester coating, 2-3 mil thickness

- Colors to be [Matthews Acrylic Polyurethane (MAP) Satin Gloss to match PMS #3025U Blue] [MAP Satin Gloss 30136 Brushed Aluminum] [MAP Satin Gloss 23966 Red] [MAP Satin Gloss 10210 Yellow] [MAP Satin Gloss 30132 Black].

PART 3  EXECUTION

  - EXAMINATION

- Verify site conditions for type of installation methodology.

- Verify that conditions are ready for product installation.

  - PREPARATION

- Coordinate and schedule installation with other site work activities.

  - INSTALLATION

- Follow manufacturer’s latest printed application and assembly instructions.

- Install product in accordance with fabricator’s instructions, these specifications, and the drawings.

- Install product in locations indicated on the drawings using mounting methods recommended by sign manufacturer, free from distortion, warp, or defect adversely affecting appearance, functionality, or warranty.

- Install product level, plumb, and at height indicated.

- [Install product at heights and distances from road edge or intersection in accordance with the Manual of Uniform Traffic Control Devices (MUTCD) and applicable local amendments and regulations.]

  - CLEANING

- Repair scratches or other damage having occurred during installation.

- Replace components where repairs were made but are still visible to the unaided eye from 10 feet.

- Clean installed product using manufacturer recommended products and in accordance with Subcontract provisions.

- Remove temporary coverings and protection of adjacent work surfaces/areas.

END OF SECTION

*************************************************************

Do not delete the following reference information:
*************************************************************

THE FOLLOWING STATEMENT IS FOR LANL USE ONLY

This project specification section is based on LANL Master Specification Section 10 1405 Rev. 4, dated December 14, 2022.