# SECTION 10 2113.13

# METAL TOILET COMPARTMENTS

*************************************************************************************************************

LANL MASTER SPECIFICATION

This template must be edited for each project.  In doing so, specifier must add job-specific requirements.  Brackets are used in the text to indicate designer choices or locations where text must be supplied by the designer.  Once the choice is made or text supplied, remove the brackets.  The specifications must also be edited to delete specification requirements for processes, items, or designs that are not included in the project -- and specifier’s notes such as these.  To seek a variance from requirements in the specifications that are applicable, contact the Engineering Standards Manual Architectural POC. Please contact POC with suggestions for improvement as well.

When assembling a specification package, include applicable specifications from all Divisions, especially Division 1, General requirements.

Specification developed for ML-4 projects.  For ML-1, 2, and 3 applications, additional requirements and independent reviews should be added if increased confidence in procurement or execution is desired; see ESM Chapter 1 Section Z10 Specifications and Quality sections.
*************************************************************************************************************

# PART 1  GENERAL

# 1.1	WORK INCLUDED

A.	Furnishing and installation of metal toilet compartments.

B.	Furnishing and installation of urinal screen(s).

# 1.2	RELATED SECTIONS

A.	Section 10 2800, Toilet and Bath Accessories

# 1.3	REFERENCES

A.	ADAAG-98, Accessibility Guidelines for Buildings and Facilities.

B.	ASTM A-167-99, Specification for Steel Sheet, Electrolytic Zinc-Coated, for Light Coating Mass Applications.

C.	FS A-A-60003, Partitions, Toilet, Complete.

D.	EPA (Environmental Protection Agency) CPG (Comprehensive Procurement Guideline), http://www.epa.gov/cpg

# 1.4	SUBMITTALS

A.	Submit the following in accordance with Section 01 3300, Submittal Procedures:

1.	Submit product data for [approval] [information] for materials, fabrications and installation.

2.	Submit shop drawings for [approval] [information] for fabrications and erection of partition assemblies no fully described by product data.

3.	Submit [standard] [custom] color [samples] [charts] for [approval] [information].

# 1.5	DELIVERY, STORAGE, AND HANDLING

A.	Deliver and store material in the manufacturer’s shipping packages.

B.	Protect material from damage.

C.	Handle material carefully to prevent damage. Unpack and install in a manner to protect the panel finish from damage.

# PART 2  PRODUCTS

# 2.1	PRODUCT OPTIONS AND SUBSTITUTIONS

# A.	Comply with Section 01 2500, Substitution Procedures.

# 2.1	GENERAL

A.	Toilet compartments are to be [overhead] [floors] braced type and include dividing panels, doors, fronts, headrail, and hardware.

B.	Handicapped toilet compartments are to comply with ADA requirements.

# 2.2	MANUFACTURERS

A.	Manufacturers offering products that comply with the requirements for metal toilet compartments include:

1.	All American Metal Corporation

2.	Global Steel Products Corporation, Embassy

3.	General Partitions Mfg. Corporation

4.	Sanymetal Products Company, Inc.

# 2.3	MATERIALS

A.	Use sheet steel conforming to ASTM A526 with G90 zinc coating.

B.	Provide attachments, screws and bolts made from stainless steel, tamper proof type; heavy duty extruded aluminum brackets.

C.	Provide hardware with chrome plated non-ferrous cast pivot hinges, gravity type, adjustable for door close positioning; nylon bearings; thumb turn door latch; door strike and keeper with rubber bumper; cast alloy chrome plated coat hook and bumper.

D.	Minimum recovered (recycled) material content 25-30 percent steel from Basic Oxygen Furnace (BOF) process or 100 percent from Electric Arc  Furnace (EAF) process in accordance with EPA’s CPG.

# 2.4	FABRICATION

A.	Fabricate partitions in accordance with FS A-A-60003.

B.	Fabricate components of steel sheet as follows:

1.	Pilasters and Fronts, 20 gage

2.	Panels and Screens, 20 gage

3.	Doors, 22 gage

4.	Concealed Reinforcement for Anchorages, 12 gage

5.	Concealed Reinforcement for Tapping, 14 gage

C.	Core Material: Standard sound-deadening honeycomb impregnated kraft paper, in thickness to provide finished dimensions of 1 inch for doors, panels, and urinal screens, and 1 1/4 inch for pilasters and fronts.

D.	Provide pilaster shoes conforming to ASTM A167 Type 304 stainless steel not less than 3 inches high, 20 gage, finish to match the hardware.

E.	Stirrup Brackets: Standard design for attaching panels to walls and pilasters of anodized aluminum to match the hardware finish.

F.	Provide internal reinforcement in areas of attached hardware and fittings.

G.	Hardware and Accessories: Standard design, heavy-duty operating hardware and accessories of nonferrous cast alloy with chrome-plated finish for coat hook/bumper, hinges and locking hardware.

H.	Anchorages and Fasteners: Standard exposed fasteners of stainless steel or brass finished to match hardware. Use theft-resistant (one-way) type heads and nuts for exposed anchorages. Concealed anchors will be hot-dip galvanized cadmium plated or other rust-resistant material.

I.	Overhead Bracing: Continuous anodized aluminum tubing, anti-grip.

# 2.5	FACTORY FINISHING

A.	Clean, degrease and neutralize panels.

B.	Follow with a phosphatizing treatment prime coat and two finish coats of baked enamel of color selected.

# PART 3  EXECUTION

# 3.1	INSPECTION

A.	Verify that site conditions are ready to receive work of this Section, and opening dimensions are as indicated on shop drawings.

B,	Verify correct spacing of toilet fixtures.

C.	Verify correct location of built-in framing, anchorages and bracing, where required.

D.	If existing conditions will adversely affect acceptable results, do not begin installation and notify the LANL Subcontract Technical Representative (STR).

# 3.2	INSTALLATION

A.	Install partitions secure, plumb and level, in accordance with approved shop drawings.

B.	Maintain 1 inch space between wall and panels, and 3/8 to 1/2 inch between wall and end pilasters.

C.	Attach panel brackets securely to walls using anchor devices.

D.	Attach panels and pilasters to brackets with through sleeve theft-proof bolts and nuts.

E.	Anchor urinal screen panel to wall with two panel brackets and vertical upright consisting of 12 inch wide pilaster stock and socket anchored to floor.

F.	Provide adjustment for floor variations with screw jack through steel saddles integral with pilaster. Conceal floor fasteners with pilaster shoes.

G.	Equip doors with 2 hinges, 1 door latch, and 1 coat hook and bumper.

H.	Install door strike and keeper with door bumper on pilaster in alignment with door latch.

I.	Adjust hinges to locate door in full closed position when latched.

# 3.3	ADJUSTING

A.	Adjust and align hardware to uniform clearance at vertical edge of doors, not exceeding 3/16 inch.

# 3.4	CLEANING

A.	Remove protective maskings, clean surfaces.

B.	Replace damaged or scratched materials with new materials.

# END OF SECTION

*****************************************************************

Do not delete the following reference information:

*****************************************************************

# FOR LANL USE ONLY

This project specification is based on LANL Master Specification 10 2113.13 Rev. 1, dated May 16, 2008.