SECTION 11 1313

LOADING DOCK BUMPERS

*************************************************************************************************************

LANL MASTER SPECIFICATION

When editing to suit project, author shall add job-specific requirements and delete only those portions that in no way apply to the activity (e.g., a component that does not apply).  To seek a variance from applicable requirements, contact the ESM Architectural POC.

When assembling a specification package, include applicable specifications from all Divisions, especially Division 1, General Requirements.

Delete information within “stars” during editing.

Specification developed for ML-3 projects.  For ML-1 / ML-2, additional requirements and QA reviews are required.

*************************************************************************************************************

PART 1  GENERAL

1.1	SECTION INCLUDES

A.	Dock bumpers of reinforced rubber with attachment frames.

1.2	SUBMITTALS

A.	Submit the following in accordance with requirements of Section 01 3300.

1.	Catalog data indicating unit dimensions, details of construction, description of materials and method of anchorage.

2.	Manufacturer’s installation instructions.

PART 2  PRODUCTS

2.1	MANUFACTURERS

A.	Durable Corporation, Dura-Dock

2.2	COMPONENTS

A.	Use bumpers made of reinforced rubber pads, ozone resistant, laminated and compressed in position with two galvanized steel rods with threaded ends, washers and nuts; between galvanized steel angle end plates.

1.	Projection from dock face:  6 inches

2.	Vertical height:  10 inches

3.	Length:  24 inches

4.	Profile:  rectangular

B.	Use galvanized 3/4 inch expansion bolts to anchor units to face of dock.

PART 3  EXECUTION

3.1	INSPECTION

A.	Verify that anchor bolt placement is acceptable.

3.2	INSTALLATION

A.	Install in accordance with manufacturer’s installation instructions.

B.	Secure end frames to concrete.

END OF SECTION

*****************************************************************

Do not delete the following reference information:

*****************************************************************

FOR LANL USE ONLY

This project specification is based on LANL Master Specification 11 1313 Rev. 0, dated January 6, 2006.