SECTION 32 9223

SODDING

*************************************************************************************************************

LANL MASTER SPECIFICATION

When editing to suit project, author shall add job-specific requirements and delete only those portions that in no way apply to the activity (e.g., a component that does not apply).  To seek a variance from applicable requirements, contact the ESM Civil POC.

When assembling a specification package, include applicable specifications from all Divisions, especially Division 1, General Requirements.

Delete information within “stars” during editing.

Specification developed for ML-3 / ML-4 projects.  For ML-1 / ML-2, additional requirements and QA reviews are required.

See ESM Civil Chapter 3, Section G2050, Landscaping and ESM Architectural Chapter 4, Section B-C_GEN, G2050 for additional guidance.

*************************************************************************************************************

GENERAL

1.1	SECTION INCLUDES

Preparation of subsoil.

Soil Amendments.

Fertilizing.

Sod installation.

Maintenance.

  - RELATED SECTIONS

A.	Section 32 8400, Planting Irrigation

1.3	SUBMITTALS

A.	Submit the following in accordance with Section 01 3300, Submittal Procedures:

1.	Sod certification for grass species and name and location of sod source.

2.	Sodding schedule, including dates and type of work to be performed.  Once accepted, revise schedule only as approved in writing by LANL Contract Administrator, after documentation of delays.

3.	Submit list of materials for approval prior to ordering and name of supplier of soil amendments materials.

1.4	QUALITY ASSURANCE

A.	Sod: Minimum of two mowings, with root development that will support its own weight without tearing when suspended vertically by holding the upper two corners.

    - Sod Producer: Company specializing in sod production and harvesting with minimum 5 years experience.

1.5	DELIVERY, STORAGE AND HANDLING

A.	Time onsite delivery so that sod will be placed within 48 hours.  Protect materials from deterioration during delivery and while stored on site.

1.6	SITE CONDITIONS

A.	Proceed with and complete landscape work as rapidly as portions of site become available, working within seasonal limitations for each kind of landscape work required.

B.	When conditions detrimental to plant growth are encountered, such as rubble fill, adverse drainage conditions, or obstructions consult the LANL Contract Administrator before planting.

C.	Plant or install materials during normal planting seasons for each type of landscape work required.  Correlate planting with specified maintenance periods to provide maintenance from date of final acceptance.

PRODUCTS

SOIL AMENDMENTS

Spread lawn starter fertilizer at a rate of 1 pound of nitrogen (N) per 1,000 sq. ft. or 1.2 to 1.5 pounds of phosphorus (P205) per 1000 sq. ft. after placing sod.

Provide a topsoil mixture to include a blend of topsoil, biocomp, compost, or peat moss installed on prepared subgrade as a bed and top dressing for solid grass sod. “Planter’s mix” topsoil is preferred.

GRASS MATERIALS

Provide strongly rooted sod, free of weeds and undesirable native grasses and machine cut to pad thickness of 3/4 inch (plus or minus 1/4 inch), excluding top growth and thatch.  Provide sod capable of growth and development when planted.

Provide sod primarily composed of tall fescue varieties.  Do not use bluegrass.  Tall fescue sod blend shall be as follows:

Triathalawn Fescue Blend- 10lbs/1000 sq. ft.

Defiance Fescue Blend - 8-10 lbs/1000 sq. ft.

Rebel Fescue Blend- 8-10 lbs/1000 sq. ft.

EXECUTION

  - PREPARATION

Preparation for Sodding

Where sod is to be planted in area that has not been altered or disturbed by excavating, grading or stripping, prepare area as follows: Strip existing grass, vegetation and turf.  Dispose of such material in area(s) designated by LANL.  Do not turn over into soil being prepared for sod.  Till area to be sodded to 4 inch depth.

Bring excavated or embankment areas to be sodded to an even grade, and shaped to provide drainage.  Level area evenly to prevent uneven settlement after installation and watering.  Final grading shall be 1 inch below hard surfaces; sidewalks, etc.

Clean areas to be sodded of roots, plants, clods, stones, clay lumps, and other extraneous materials harmful or toxic to plant growth.

Spread pre-mixed soil material to an even 2 inch minimum depth over subgrade.  Rototil pre-mixed soil into the top 4 inches of subgrade, thoroughly mixing in cross directions.  Drag to even grade, then roll for firmness with a minimum 300-pound roller.

Rake tilled area and remove stones over 1 inch in any dimension, sticks, roots, rubbish and other extraneous matter.

Install sod adjacent to landscape edging, walks, and curbs abutting the edging, walk, or curb edge with top of grass to be one inch below top of walk or curb.

Limit preparation to area that will be planted within 48 hours after preparation.

Restore grading to specified condition if eroded or otherwise disturbed after fine grading and prior to sodding.

Spread starter fertilizer at a rate of 1 pound of nitrogen (N) per 1,000 sq. ft. or 1.2 to 1.5 pounds of phosphorus (P205) per 1000 sq. ft. after placing sod.  Delay application of fertilizer, if sod planting will not follow within 24 hours.

Installation of irrigation systems, trees and shrubs, and edging material shall be completed and tested before sodding.

SODDING OPERATIONS

Do not plant dormant sod or place sod on frozen ground.

If soil is dry, moisten areas before sodding.  Water thoroughly and allow surface moisture to dry.  Do not create a muddy soil condition.

Lay sod to form a solid mass with tightly fitted joints without stretching the sod.  Ends and sides of sod strips shall not overlap.  Stagger strips to off-set joints in adjacent courses.  Lay sod parallel to contours of slope.

Tamp firmly and evenly by hand to ensure contact with subsoil.  Work sifted topsoil or sand into minor cracks between pieces of sod; remove excess to avoid smothering grass.  Roll entire area with weighted hand roller.

Do not tear the sod.  Cut and trim sod with a sharp, stiff knife.  Avoid small pieces and strips.

Thoroughly water sod to prevent drying or wilting immediately after planting.

MAINTENANCE

Maintain lawns for not less than the period stated below, and longer as required to establish an acceptable lawn.  Perform maintenance in a manner that will promote a healthy thick, even stand of grass.

Sodded lawns to be maintained not less than 30 days after final acceptance, or through the October 1 growing season, whichever is longer.

Irrigate sodded areas by means of the automatic underground irrigation system, or other means, as often as necessary to promote healthy grass growth until a thick, even stand of grass has been obtained.

Maintain lawns by watering, fertilizing, weeding, mowing, trimming, and replanting as required to establish a smooth, acceptable lawn, free of eroded or bare areas.  Mow the lawn with a mulching mower approximately two weeks after installation or when reaching a blade height of 2 ½ inches.  Do not cut off more than 1/3 of the blade height.

CLEANUP AND PROTECTION

During the work, keep pavements clean and work area in an orderly condition.

Protect sodded areas, work and materials from damage due to vehicles, pedestrians, and operations by other contractors.  Maintain protection during installation and maintenance periods.  Treat, repair or replace damaged work as directed.

Upon completion of all sodding operations, clean the portion of the project site used for storing materials and equipment of all debris.  Remove all superfluous materials and equipment from the project site.  Sweep walks and pavement clean upon completion of work in this section.

INSPECTION AND ACCEPTANCE

When inspected work does not comply with requirements, replace rejected work and continue with specified maintenance until reinspected by LANL and found to be acceptable.  Remove rejected sod and materials promptly from project site.

END OF SECTION

****************************************************

Do not delete the following reference information:

****************************************************

FOR LANL USE ONLY

This project specification is based on LANL Master Specification 32 9223 Rev. 1, dated October 31, 2006.